PARAMETER OF PAPER CUP MACHINE

| Model | DB-L12 DB-2L12 | DEBAO-X16 DEBAO-2X16 | DEBAO-600A |
| --- | --- | --- | --- |
| Production capacity | 45-55pcs/min | 50-60pcs/min | 80-90pcs/min |
| required paper | 150-250gsm for one side PE coated paper 150-380gsm for double PE coated paper (Ultrasonic control) | 150-250gsm for one side PE coated paper 150-380gsm for double PE coated paper (Ultrasonic control) | 230-350gsm |
| container capacities | (A)top dia: ¢50-90mm (B)height: 45-115mm (C)bottom dia:¢35-64mm (D)knurling: 4.5-10mm (Suit for paper cups at 2.5-12OZ ) | (A)top dia: φ70-100mm; (B)height: 60-135mm; (C)bottom dia: φ45-75mm; (D)knurling: 5-12mm (Suit for paper cups at 8-16OZ) | (A)top dia: φ60-95mm; (B)height: 70-135mm; (C)bottom dia: φ45-65mm; (D)knurling: 5-12mm (Suit for paper cups at 6-12OZ) |
| total power | 220v50hz3.8/8kw or 380v50hz 3.8/8kw (variable-frequency control) | 380V 50HZ 5/9KW | 380V 50HZ 18KW |
| weight | 1300kg | 1800kg | 2000kg |
| overall dimensions | 2.55m×1.26m×1.7m | 2.8×1.4×1.8m | 2.5×1.4×1.9m |

# Text boxes

DB-L12 paper cup machine advantages:

- The frame of main frame of the machine is an incline, make the cups easy drop into the plastic hole,the rate goes up to 99.9%.

- The shape of the head is oblate, which can seat the cups easily.It is much better than that is round.

- The machine sends the bottom paper up to the cup automatically and adjust itself because of a spring.

DEBAO-X16 paper cup machine advantages:

- It is designed drum-type cam indexing and positioning instead of indexing box

- Optimization of the feeding part, it can reduce paper jams

- The shape of the head is oblate, which can seat the cups easily.It is much better than that is round.

- The machine sends the bottom paper up to the cup automatically and adjust itself because of a spring

DEBAO-600A paper cup machine advantages:

- It is designed with drum-type cam indexing and positioning,which offers high precision indexing and positioning as a result of its good inertia-resistance capability.

2. Mechanical transmission parts use gear of longitudinal axis to ensure continuity of action and machine stability, to prevent machine collisions

3. Photoelectric failure-detecting system is available. PLC control system for the whole cup forming process . Servo control to send bottom paper of cup, deliver bottom when cup tube come, otherwise no bottom delivery.

4. Switzerland Leister heating device is equipped on cup body and bottom adhesion step .Cup-bottoms are heated at first before they are fed ,thus improving heating effect and helping guarantee knurling quality.

5. Machine use box type structure design, filling the oil by spray lubrication system, to make machine running fast