# Hose crimping machine KM-91L

☆ Advantage:

1. With cartridge valve, the machine is steady and reliable.

2.There is the lubrication and dustproof system.

3.  Two option of control modes: normal

and computer.

4.  Option: quick change tool.

Technical data:

| Crimp range | 1 1/4"，1 1/2" ，2 " 6SP |
| --- | --- |
| Standard voltage & motor | 220V/2.2kw |
| Opening without dies | 122mm |
| Opening | ±28mm |
| Swaging force | 7600KN |
| Open | 1.5s |
| Close | 11s |
| Optional voltage motor | as customer’s requirement |
| No. of standard die set | 3 sets |
| Systematic pressure | 31.5Mpa |
| L*W*H | 690mm*465mm*790mm |

- Special:

- NEW foam inserts introduced to protect your machine

from debris dropping into the bottom of the head. With

there you will minimize the risk of debris getting into

the cylinder which could cause damage to seals and

other moving parts of the head. This will significantly extend the life of hydraulic hose crimping machine.

2. The machine head connect by bolts

Result: NO leakage and damage.

☆Die chat:

◇We are able to offer you special equipment which meet your expectations and improve your comfort and efficiency.

◇Our principle: it bases on technology, innovation and service to large the market.