MQ-320 Roll-roll Adhesive Label Die Cutter Machine

Characteristics: 
This is a high precision flat-bed die cutter machine. Material feeding & cutting are controlled by servo motor. Lateral sides are controlled by 2pcs of sensor and lineal side is controlled by one of sensor. Laminating, die cutting, waster removal, sheeting or rewinding can be completed in one pass. It is suitable for cutting pressure sensitive label and holographic anti-counterfeiting label. It is a best, efficient partner for adhesive label printing machine and hologram die cutter and is also applicable for label house, electronic parts die cutting and adhesive tape sectors.

Options :
1. hot foil device

2. Lamination device
3. Sprocket device

Technical specification:

| Cutting speed | 20-180 cycle/min |
| --- | --- |
| Max. unwind diameter | 500mm |
| Max. Web width | 320mm |
| Max. die cutting width | 300mm |
| Max. die cutting length | 290mm |
| Positioning accuracy | +-0.1mm |
| Total capacity | 2.7kw |
| Power | 220v |
| Overall dimensions(L*W*H) | 2800*1100*1600mm |
| Machine weight | About 1500kg |