无锡贝瑞斯机械设备有限公司

WUXI BALANCE MACHINERY EQUIPMENT CO., LTD

Add: D1112, No.158, Wangzhuang Road, Wuxi City, Jiangsu Province, China

Tel: 0086-510-83115339    Fax: 0086-510-83113616    Mobile: 0086-158-616-98920

Skype: platform_balance       MSN: platform_balance@hotmail.com

Email: angela@cnplatform.com            Web: www.cnplatform.com

Contact: Angel Wang

QUOTATION

To: Mr. Jose Ira

| Mast Aerial Work Platform |
| --- |
| Model | Platform Size (m) | Lifting Height (m) | Motor Power (kw) | Power (v) | Rated Capacity (kg) | Qty (Set) | FOB SHANGHAI PORT, CHINA (USD) |
| GTWY6-200S | 1.48*0.6 | 13 | 1.5 | 220 | 200 | 1 | US$ 4,440 / SET |

Above includes the following items:

| No. | Name | Configuration |
| --- | --- | --- |
| 1 | Main Material | 6005 High strength aluminum alloy |
| 2 | Manual Pump | 2 Sets |
| 3 | Chassis Material | 100*50*4 Manganese steel rectangular tube 4mm Steel plate |
| 4 | Platform Material | 3mm Diamond plate |
| 5 | Guardrail Specification | Square tube, 1000mm high |
| 6 | hydraulic oil cylinder | Φ40 mm*2 pcs |
| 7 | Transmission chain | Plate link chain LL0844 chain |
| 8 | Hydraulic Medium | 32# anti-wear hydraulic oil |
| 9 | Moving Wheels | Heavy-duty polyurethane wheels, 4 Pcs |
| 10 | Sealing Element | HUP, Y type sealing element, Rubber O -rings |
| 11 | Surface Treatment | Plastic coating procession |
| 12 | Balance Device | Must adjust balance before lifting and descending |
| Note: 1. Lifting speed: 6m/min Descend speed: 0-10m/min, adjustable. 2. The product equips descent device when emergency, over-loading protection device. |

Summary:

- Terms of validity: 1 month

- Payment: USD 100% paid in advance by T/T.

3.  Time of Delivery: 10-15 working days after receipt of the payment.

4.  Warranty: 1 year

5.  Package: Nude packing