ZG型真空制膏机系列

ZG Vacuum Paste Machine Series

真空制膏机系列广泛用于牙膏、化妆品、食品、化工等行业粘稠膏体的制造。全套设备配有制膏机、预混锅、胶水锅、粉料斗、胶体泵、操作平台。

The vacuum machine produced by our company is widely used for manufacturing paste-like products of toothpaste, comsmetics , foods and chemistry industry, etc.. This equipment includes paste machine, pre-mix boiler, gluewater boiler, powder material hopper, colloid pump and operation platform.

主要技术参数（Main Technical Parameters）

| 型号 Type | ZG-100 | ZG-700 | ZG-1300 |
| --- | --- | --- | --- |
| 工作容量 Cubage(L) | 100 | 700 | 1300 |
| 真空泵 Power of Vacuum Pump(kW) | 3 | 4 | 7.5 |
| 液压泵 Hydraulic Pump(kW) | 1.1 | 1.5 | 2.2 |
| 锅盖升降高度Lifting Height of Vessel cover(mm) | 800 | 1000 | 1000 |
| 外形尺寸 Dimensions(L×W×H) (mm) | 2450×1500×2040 | 4530×3800×2480 | 1920×3910×3200 |
| 整机重量 Weight(kg) | 2500 | 3000 | 4500 |