H-beam Combination Work Station

H型钢组焊矫一体机

机器型号Machine model: ZHJ

报价编号Offer refer:130322EC

摆布图Lay-out:

- 机器包装尺寸Machine packing dimension: 11800mm×2130mm×2300mm

- 总毛重Total G.W: Approx 21000 kg

- 建议集装箱Suggest container: 40'HC

可加工H型钢规格H-beam dimensions:

- 翼缘板宽度Flange width: 200-800mm

- 翼缘板厚度Flange thickness: 8-40mm

- 腹板高度Web height: 300-2000mm

- 腹板厚度Web thickness: 6-30mm

- 工件长度H-beam length: 6000-15000mm

机器参数Machine parameter

- 焊接方式Welding type: 自动双边埋弧焊automatic double-side submerged-arc welding

- 定位方式Positioning type: 导向丝杠guide screw

- 控制方式Speed control type: 深圳汇川交流变频器Shenzhen Inovance Ac frequency inverter

- 焊接角度Welding angel: 45度可调45 degree (adjustable)

- 生产速度Line speed: 400-1000mm/min

- 焊机型号Welder power model: 成都福田ZD5-1000埋弧焊机Chendu FOT ZD5-1000 submerged arc welder

- 电压Voltage: 380 V/50 Hz

- 总功率Total power: 150kW

- 安装空间Installation space: 35000mm×3000mm×5000mm

供应范围Supply Scope

- 主机Frame assembly.

- 电控系统Electric control system: electric cabinet, etc.

- 组立机构Assembly device

- 抬升装置1号Hold device 1#

- 出料输送辊道Out-put conveyor (包含抬升装置2号Included hold device 2#)

- 液压系统Hydraulic system

- 提升装置Lifting device

- 焊丝送丝机构Welding wire feeding device

- 工作平台Work platform

- 梯子Staircase

- 焊机Welder power

- 焊剂回收机Flux recovery

技术文件Technical Document

- 操作手册Machine operation manual

- 安装图纸Installation drawing

- 电气原理图Electrical circuit diagram

- 发货清单Supply list

- 合格证Qualified certificate

价格Price：USD73,580 (FOB Shanghai, China)

交货期Production lead time：within 60 days

付款方式Payment：30%T/T in advance, 70%T/T before shipment