| HUADA |  |
| --- | --- |
|  | Add.: Industrial Building, Huaqiao University, Quanzhou City, Fujian, China Tel: +86-595-22691763 Fax: +86-595-22692763 E-mail: diamond16@hqutool.com Website: www.hqutool.com |

Quotation

1-1. AUTOMATIC wire saw machine for marble quarry

| Model | Main motor power | Length of wire (m) | Line speed (m/s) | USD/set |
| --- | --- | --- | --- | --- |
| DWS-37AX-6P | 37kw (50HP) | 20~80 | 0~40 | 15,200 |
| DWS-45AX-6P | 45kw (60HP) | 20~100 | 0~40 | 16,500 |
| DWS-55AX-6P | 55kw (75HP) | 20~120 | 0~40 | 18,500 |
| DWS-75AX-8P | 75kw(100HP) | 20~150 | 0~40 | 23,000 |
| DWS-110AX-8P | 110kw(150HP) | 40~180 | 0~50 | 31,700 |
| Function: | 1. Controlled by dual inverter + PLC, make the diamond wire saw strain constantly and the speed of moving truck automatically controlled. 2. When under the automatic control state, the machine can track changes in the load so as to make the diamond wire saw work efficiently all the time by adjusting the move speed of the machine. 3. Protect the diamond wire saw from break, overload, lack of phase, terminal limit. 4. Easy-operating functions of electric turnover, electric horizontal movement and quick moving. |
| Accessory: | three pieces rail(2 m*3)/ one pc of big fly wheel and four pcs of small flywheels/ one pc hydraulic presser/ one pc scissor |
| Remark: | Both the line speed and move speed can be automatically changed. |

1-2. AUTOMATIC wire saw machine for granite quarry

| Model | Main motor power | Length of wire (m) | Line speed (m/s) | USD/set |
| --- | --- | --- | --- | --- |
| DWS-37AX-8P | 37kw (50HP) | 20~80 | 0~30 | 15,500 |
| DWS-45AX-8P | 45kw (60HP) | 20~100 | 0~30 | 18,300 |
| DWS-55AX-8P | 55kw (75HP) | 20~120 | 0~30 | 19,500 |
| DWS-75AX-8P | 75kw(100HP) | 20~150 | 0~30 | 23,000 |
| DWS-110AX-8P | 110kw(150HP) | 40~180 | 0~50 | 31,700 |
| Function: | 1. Controlled by dual inverter + PLC, make the diamond wire saw strain constantly and the speed of moving truck automatically controlled. 2. When under the automatic control state, the machine can track changes in the load so as to make the diamond wire saw work efficiently all the time by adjusting the move speed of the machine. 3. Protect the diamond wire saw from break, overload, lack of phase, terminal limit. 4. Easy-operating functions of electric turnover, electric horizontal movement and quick moving. |
| Accessory: | three pieces rail(2 m*3)/ one pc of big fly wheel and four pcs of small flywheels/ one pc hydraulic presser/ one pc scissor |
| Remark: | Both the line speed and move speed can be automatically changed. |

2. D-T-H Drilling Machine

| Model | Pneumatic D-T-H Drilling Machine [QZ65-90B] | Pneumatic & Electric D-T-H Drilling Machine [QDZ65-90B] |
| --- | --- | --- |
| Max. depth of drilling | 35~40m | 35~40m |
| Diameter of drilling | 90mm | 90mm |
| Drilling speed | 6~8m/h | 6~8m/h |
| Minimum air pressure | 0.5~0.7MPa | 0.5~0.7MPa |
| Total compressed air consumption | 12~14m³/min | 7~9 m³/min |
| Track travel | 1m | 1m |
| Advance device | Pneumatic motor, reducer, chain | Pneumatic motor, reducer, chain |
| The pneumatic rotation head | Pneumatic motor, reducer | Motor, reducer |
| Drilling direction | Any direction | Any direction |
| USD/set | 4900 | 4750 |

3. Horizontal Core-boring Machine

| Model | WQZ80 | WQZ80B |
| --- | --- | --- |
| Drilling hole diameter | 80mm | 80mm |
| Max. drilling length | 40m | 40m |
| Speed of drilling hole | 3~12m/h | 3~12m/h |
| Min. water supply pressure | 0.1MPa | 0.1MPa |
| Single advance stroke | 1.5m | 1.5m |
| Rotation device | Motor + reducer | Motor + reducer + inverter |
| Advance device | Chain + reducer | Chain + reducer |
| Drilling direction | Horizontal | Horizontal |
| Control method | Moving automatic control Main motor constant speed | Moving automatic control Main motor speed is adjustable |
| USD/set | 4600 | 5700 |

4.Rock Driller Machine

| Model | Two-Hammer Rock Driller for Vertical and Horizontal Drilling(Heavy Type) [CZH-24/28-2B] | Four-Hammer Rock Driller(Heavy Type) [CZ-24/28/29-4B] |
| --- | --- | --- |
| Rock driller | 2-YT24/2-YT28 | 2-YT24/28/29 |
| Rated track length | 2*3m | 2*3m |
| Max. Drilling depth | 6m | 6m |
| Drilling diameter | ￠34mm~￠42mm | ￠34mm~￠42mm |
| Minimum air pressure | 0.5--0.7MPa | 0.5--0.7MPa |
| Drilling speed | 2*30m/h | 4*40m/h |
| Total compressed air consumption | 10m³/min | 20m³/min |
| Track travel | 2m | 2m |
| Advance device | Pneumatic motor, chain | Pneumatic motor, chain |
| Cross travel device | Handwheel, gear, rack | Handwheel, gear, rack |
| Drilling direction | Any direction | Any direction |
| Number of the hole hammer | 2 | 4 |
| Total weight | 1000Kg | 1100Kg |
| USD/set | $ | $ |

5. Diamond wire saw for marble/granite quarry

| Specification | USD/meter |
| --- | --- |
| 11.5mm, rubber, 40 beads/meter | 47(marble) 50(granite) |

Price term: FOB XIAMEN

Payment terms: 30% T/T in advance, the balance 70% T/T before shipment

Delivery time: within 30 days after receiving deposit

Package: carton and crate

Albee Lin

2013-04-29