Conjunto da máquina de sopra de filme de polipropileno com cabeça rotativa

SJ-60/FM600

Características:

Os cilindros e os hastes de parafusos do extrusor são feitos de aço de liga de alta qualidade com ótima dureza e resistência à corrosão forte após o acabamento de precisão e tratamento de nitrogénio.

O extrusor pode ser elevar-se até a 3 m de acordo com os requisitos tecnológicos. Modo de sopro de filme; sopro de parte inferior, a unidade de bobinamento adota o motor de torque para manter a tensão adequada e fazer com que a mudança de rolo seja fácil.  
Uso:

Ele é usado para sopro de polietileno (PP) e também para sopro de polietileno de alta e baixa intensidade (HEPE, LDPE) que são amplamente usados para embalagem de alimento, vestuário, produtos de necessidades diárias, têxteis, produtos industriais, etc.

Principoais variáveis técnicas:

| Modelo | SJ-60/FM600 |
| --- | --- |
| Diâmetro do parafuso | 60mm |
| Prporção L/D do parafuso | L/D28:1 |
| Velocidade rotativa do parafuso | 10-100r/min |
| Potência do motor principal | 15KW |
| Modo rotacional da cabeça da máquina | Gira constantemente |
| Saída principal | 38kg/h |
| Largura máxima de dobragem de filme | 600mm |
| Espessura de um lado do filme | 0.01-0.10mm |
| Potência total | 28Kw |
| Peso da máquina | 2900kg |
| Dimensão total | 4800x2000x4000mm |

SJ-500/FM600 Ratory Machine Head Polypropyleme Film Blowing

Machine Set Technology Configuration

Main prameter:

Applied Materials:PP、LDPE、HDPE

Maximum folding width of film :600mm

Single-sided thickness of film:0.01-0.10mm

Most in the extrusion quantity:38Kg/h

Standard layout

1.1 extruder

1.1 Screw:Screw Diameter 60mm; L/D Ratio:28∶1：Material：38CrMoALA

1.2. Screw Rotary Speed:：：10-100r/min

1.3. Machine barrel:Barrel Heating Cast Aluminum heating ring

Barrel cooling: a district cooling,cooling fan :350W

1.4 Temperature control mode: automatic control of 3 district

1.5 Reducer:hardened reducer

1.6 Out of the main motor :converter motor

- Screw changer

2.1 Manually remove the screen changing device

2.2 The exchanger heating :cast aluminum heating ring

2.3 Temperature control mode:antomatic temperature control zone1

- Die head

3.1 Basic structure :single screw die head structure

3.2 Die material:40Cr die steel

3.3 Specification of die orifice:φ250mm

3.4 Die head heating:cast aluminum heating ring

3.5 Temperature control mode:automatic temperature control zone1

- Rotating head

4.1 Structure :rotating head 360°long running

4.2 Ratory motor power:0.37Kw

4.3 Temperature control mode: automatic temperatrue control zone 2

- Vane

5.1 Structure :Single inlet air ring

5.2 Material:cast aluminium

5.3 The power of fan:1.5KW

- Water ring

6.1 Material:cast aluminium

6.2 Specifications:configured with 4 pieces(size according to customer’s requirement)

- Collapser

7.1 Structure:Stainless steel

7.2 Adjusting mode:hand movement

- The first traction

8.1 Structure :Stationary type

8.2 Pulling motor:converter motor

8.3 The clamping way of carry-over pinch roll

- The second traction

9.1 Structure :Stationary type

9.2 Pulling motor:converter motor 1.1LKW(and the first traction with one motor

9.3 The clamping way of carry-over pinch roll: the mechanical clamping device

- The third traction

10.1 Structure::Stationary type

10.2 Pulling motor:converter motor 1.1KW(ANDd the first traction with one motor)

10.3 The clamping way of carry-over pinch roll:the mechanical clamping device

- Air drying machine

- Coiling machine

QUOTAÇÃo:

| Modelo | FOB Ningbo (USD) |
| --- | --- |
| SJ-60/FM600 | 14100 |

Observações:

Pagamento: 30% de pagamento antecipado, 70% deve ser pago quando a mercadoria estiver pronta .

Embalagem: Embalagem de filme de plástico

Entrega: 20 dias após o recebimento de depósito

Garantia : um ano

Dentro deste período, todas as peças quebradas naturalmente, não pelo erro humano, nós podemos substituir gratuitamente. Mas o comprador tem que enviá-las de volta para nós. Após este período,  podemos substituir as peças danificadas, mas cobramos os preços originais

Vicky

6 de Abril de  2013