无锡贝瑞斯机械设备有限公司

WUXI BALANCE MACHINERY EQUIPMENT CO., LTD

Add: Baolu Road, Qianzhou Industrial Zone, Huishan District, Wuxi City, Jiangsu Province, China

Tel: 0086-510-83115339    Fax: 0086-510-83113616    Mobile: 0086-158-616-98920

Skype: platform_balance       MSN: platform_balance@hotmail.com

Email: angela@cnplatform.com            Web: www.cnplatform.com

Contact: Angela Wang

QUOTATION

To: Mr. Raymond                                   Quote No.: 13BRS030604

| Fixed Scissor Lift Work Platform |
| --- |
| Model | Configuration | Quantity |
| SJG2.5-2 | Shut Height (mm) | 480 | 1 Set |
|  | Lifting Height (mm) | 2000 |  |
|  | Max. Platform Height (mm) | 2480 |  |
|  | Table Size (mm) | 3200*2500 |  |
|  | Rated Capacity (kg) | 2500 |  |
|  | Motor Power (kw) | 4.0 |  |
|  | Hydro cylinder | Φ100mm (2 pcs) |  |
|  | Voltage | 230V/3 Phases/60Hz |  |
| FOB SHANGHAI PORT, CHINA ------ US$ 4,800 / SET (It will be delivered by LCL with other clients’ products.) The fixed lifting platform need digging pit first. We will supply you the pit drawing after we do the transaction. |

Above includes the following items (SJG2.5-2):

| No. | Name | Configuration |
| --- | --- | --- |
| 1 | Material of platform | 5 mm antiskidding diamond plate Guardrail 1000mm |
| 2 | Platform framework | Q345B high strength manganese steel 100*40*4 rectangular tube |
| 3 | Main beam of Scissor material | Q345B high strength manganese steel 180*65*6 rectangular tube |
| 4 | Hydro cylinder | Diameter: 100mm (2 pcs) |
| 5 | high-pressure oil tube | High pressure Double-layer steel mesh rubber hose 602-0802-48.0MPa |
| 6 | hydraulic medium | 32# hard wearing hydraulic medium |
| 7 | (Electrical) appliance | Relay, Contactor, Button, etc |
| 8 | sealing element | UHP, Y type sealing element, Rubber O -rings |
| 9 | Power unit | 4.0kw (Motor, Wheel pump and solenoid valve integrally) |
| 10 | Voltage | 230V/ 3 Phases/ 60HZ |
| Note: 1. The connecting material adopt gas shielded arc welding ( It is harder, longer-life and higher level than normal electric welding) 2. The product equips descent device when emergency, explosion prevention device, over-loading protection device. 3. Center pin and edge pin: heat treatment |

Summary:

- Terms of validity: 1 month

- Payment: USD 100% paid in advance by T/T.

3.  Time of Delivery: 20-30 working days after receipt of the payment.

4.  Warranty: 1 year