P8 食人鱼租赁显示屏

product feature

1.Eagle eye lamp,excellent image quality,wide viewing angle and colorful

2.die-casting aluminium rental cabinets

3.for both outdoor fixed with rental use with moderate viewing

4.Hanging organization dedicated  connection with the vertical approach, to achieve free lifting

5.thin structure design and light weight,great convenience to event show in transportation and installation

6.easy to connect,fast assembly

7.can be connected seamlessly to next panel

8.Random combination

Application

Trade shows,exhibitions,stages,conferences,product launches and corporate events

| Outdoor Die casting rental cabinets |
| --- |
| parameter |
| Pixel pitch | 8mm |
| enviroment | outdoor |
| density | 15625 |
| Pixel composing | 1R1G1B(Eagle eye) |
| Module resolution | 40*20dots |
| Module size | 320mm*16mm |
| Cabinet resolution | 80*80dots |
| Cabinet size | 640mm*640mm |
| Cabinet weight | 17.5KGS |
| Cabinet material | Aluminium die casting |
| Viewing angle | H110°/V110° |
| Refresh rate | 900HZ |
| Maximum power comsuption | 680W |
| Average power comsuption | 340W |
| Scan mode | 1/5 constant current |
| brightness | >6000CD/㎡ |
| Power supply demand | AC220V/110V,50Hz/60Hz |
| Working temperature | -20℃--60℃ |
| Working humidity | 10%RH~90%RH |
| Gray scale | 4096 |
| Operating platform | Windows 2000,XP,VISTA OS |
| Running files | Texts,animation,pictures,videos and etc |
| Control distance | CAT5:<100m; Single cable:<10km |
| Ingress protection | Front:IP65,Rear:IP54 |