Quotation for Semi-automatic Capsule Filling Machine

DTJ-C

DATE: June 17th, 2013

#### Attn:

#### M/S:  JOSE ANGEL PADILLA CAMBEROS

ADD:

Tel: (461) 61 42177 / (461) 6147495

Fm: Tianhong Pharmaceutical Machinery Co., LTD

Table of contents

Ⅰ PRICE AND PURCHASE ITEMS

1. Particular

2. General terms and conditions

Ⅱ MACHINE DESCRIPTION

- Technical specification

- Features

- Machine details

Ⅲ MACHINE ELECTRIC COMPONENT LIST

Ⅳ PACKING LIST

#### Ⅴ MOULD LIST

Ⅵ QUALITY TEST

Ⅳ MEDICINE POLISHER

Ⅰ PRICE AND PURCHASE ITEMS

| No | Particulars | Rate/Each US $ |
| --- | --- | --- |
| 1 | DTJ-C Semi-automatic Capsule Filling Machine The price USD 6,200 is included one whole set of mould/capsule size change parts, one vacuum pump, and one operation manual documents and training CD together with the machine. | USD6,200 |
|  | Optional Parts: |
|  | Extra Ring | USD350 |
|  | Extra complete mould for different sizes of capsule | USD700 |
|  | Accessories: |
|  | Capsule Polishing Machine | USD800 |
| 2 | General Terms and Conditions |
|  | Terms of Payment |
|  | 30% deposit in Advance remittance by Wire transfer (T/T) and the balance should be paid before shipment. |
|  | Delivery Terms |
|  | Fob Ningbo |
|  | Delivery Period |
|  | 15 days or earlier from the date of receipt of your confirmed Purchase Order along with Advance remittance. |
|  | Validity |
|  | Our offer is valid for 15 days from the date hereof and thereafter to our written confirmation. |
|  | Packing Details |
|  | Dimension: 1800*800*1800MM Weight: 550kg Export standard wooden box |
|  | Origin |
|  | The people’s Republic of China |
|  | Inspection |
|  | To be finalized by the manufacturer. If there are additional inspection requirement by the buyer or of the third party, the expense shall be deemed towards the buyer. |
|  | FAT |
|  | FAT charge covers for the inspection procedure, labor cost, and FAT document and local transportation charge. Round trip air ticket and hotel accommodation are to be expensed by customer. FAT will be progressed mechanically without batch trial. |
|  | Installation |
|  | The machine will be assembly in our workshop. We will dispatch our technician to your site to do the installation after we receive your confirmation for the pre-installation readness. All the expenses including the roung-trip air ticket, local conveyance to your factory, lodging and boarding expenses should be payable by you. Incase the stay of our technician, the service changes for US 70 per day will be charged extra. |
|  | Warranty Period |
|  | The guarantee period will be given 12 months, which starts from the date of the machine’s arrival. During this warranty period, the seller will provide free spare parts that caused by the machine’s quality within 10 days by fast courier upon receipt of buyer’s notice, with one condition that the freight shall be effected by the buyer. |

Ⅱ MACHINE DESCRIPTION

- Technical Specification:

| Max. Output | 20,000 capsules/hour |
| --- | --- |
| Suitable for Capsule | 00,0,1,2,3,4 |
| Vacuum Pump | XD-040(40M3/H) |
| Noise | <60dB(A) |
| Capacity of air compressor | 0.1m3/min |
| Net weight | 330kg |
| Gross weight | 525kg |
| Overall Dimension | 1200*700*1600mm |

2. Features:

● Equipped with independent empty capsule feeding station, powder feeding station and capsule closing station

● The filling amount can be adjusted by the number of rotations of the dosing disk. The powder feeder also has agitator to regulate the powder filling. 
● It has an infinite variable speed of filling table with independent power and fixed point filling that results in accurate dosage.
● Powder material feeding is accurate
● Machine body and working table made of stainless steel

● After all the empty capsules have been rightly rectified and filled up, the mechanism will stop automatically to reduce the operators working worries.
● Meet the GMP requirements of the pharmaceutical industry
● Suitable for filling powder and granular materials in pharmaceutical and health food industries
● The light-touch switches, feeding propeller and filling rotary table can be in
automatic run based on preset and frequency speed control.
● A special design allows for changing mould for different size capsules within 30 minutes easily, simply, and precisely.

● Only one operator is required, and operating training can be done in 10 minutes
● The machine comes with one set of capsule sized changeable parts, training video, dual capsule rings, pump unit and water recycling system.

3. Machine Details

PLC CONTROL PANEL

CAPSULE LAYING STATION

CAPSULE HOPPER

POWDER FILLING AND EJECTING STATION

ELECTRIC PARTS

Ⅲ MACHINE ELECTRIC COMPONENT LIST

| Order No. | Name | Model | Unit | Quantity | Remark |
| --- | --- | --- | --- | --- | --- |
| 1 | Transducer | HLPA00D423C | Pcs | 2 |  |
| 2 | Air circuit breaker | 3P－20A | Pcs | 1 |  |
| 3 |  | 1P－3A | Pcs | 1 |  |
| 4 | Transformer | JBK3－100 | Pcs | 1 |  |
| 5 | AC contactor | CJX2－0910 | Pcs | 3 | AC36V |
| 6 | Relay | JQX－13F | Pcs | 1 | AC36V |
| 7 | Auxiliary contact group | F4-11 | Pcs | 3 |  |
| 8 | Time relay | JSZ3(ST3P) A-B | Pcs | 1 | AC36V |
| 9 | Phase failure & phase sequence protector | XJ3-G |  | 1 | AC380V |
| 10 | Counter | N－482A | Pcs | 2 | AC36V |
| 11 | Urgent stop switch | Y090(11TS) | Pcs | 1 |  |
| 12 | Mushroom switch | LAS1－A Light: AC12V | Pcs | 4 | Red |
| 13 |  |  |  | 4 | Green |
| 14 | Rectangular switch | LAS1－A Light: AC12V | Pcs | 1 | Red |
| 15 |  |  |  | 1 | Green |
| 16 | Travel switch | LXW5－11GI | Pcs | 1 |  |
| 17 | Voltmeter | 0－300V（50×28） | Pcs | 1 |  |
| 18 | Connecting terminal | JF5－2.5/5 | Pcs | 3 |  |
| 19 |  | JF5－1.5/5 | Pcs | 5 |  |
| 20 | Hall switch | H12-D5NK | Pcs | 1 |  |
| 21 | Proximity switch | E3－D4NK－K | Pcs | 1 |  |
| 22 | Small self restoring Button | Φ10 | Pcs | 2 |  |
| 23 | Industrial plug & socket | ZM14-16A | Set | 1 |  |

Ⅳ PACKING LIST

| Order No. | Name of spare parts | Specification | Unit | QTY | Design code |
| --- | --- | --- | --- | --- | --- |
| 1 | Adjusting foot disc |  | PCS | 4 |  |
| 2 | Diagonal wrench | 8″ | PCS | 1 |  |
| 3 | Spiral tool of crisscross | 4 inch | PCS | 1 |  |
| 4 | Spiral tool of bolt | 4 inch | PCS | 1 |  |
| 5 | Hexagonal socket | 3, 4, 5, 6, 8, 10 | PCS | 1 |  |
| 6 | Pressure oil can |  | PCS | 1 |  |
| 7 | Powder shovel | JTJ-IV-05-01 | PCS | 1 |  |
| 8 | Powder cover | JTJ-IV-05-02 | PCS | 1 |  |
| 9 | Powder scrapper | JTJ-IV-05-03 | PCS | 1 |  |
| 10 | Scratch awl | JTJ-IV-05-04 | PCS | 1 |  |
| 11 | Crochet hook | JTJ-IV-05-05 | PCS | 1 |  |
| 12 | Switch wrench | JTJ-IV-05-06 | PCS | 1 |  |
| 13 | Vacuum pump | XD-0.40 | PCS | 1 |  |
| 14 | Vacuum filter | X-200 | PCS | 1 |  |
| 15 | Certification |  | PCS | 1 |  |
| 16 | Packing list |  | PCS | 1 |  |
| 17 | Manual |  | PCS | 1 |  |
| 18 | Manual of vacuum pump |  | PCS | 1 |  |
| 19 | Manual of transducer |  | PCS | 1 |  |

#### Ⅴ MOULD LIST

| Name | Quantity | Material |
| --- | --- | --- |
| Capsule-Dispensing Pipe | 1 | Copper |
| Capsule –Pressing Head | 1 |  |
| Capsule-Carrying Switch | 1 |  |
| Capsule-Carrying Comb | 1 |  |
| Capsule-carrying Comb Base | 1 |  |
| Capsule-Driving Plate | 1 | Aluminum Alloy |
| Pin Disk | 1 | Base: cooper Pins: SS 304 |
| Capsule Ring | 1 | Aluminum Alloy |

Ⅵ QUALITY TEST

| In order to ensure the quality, Semi-Automatic Capsule Filling Machine is accepted the Quality Test every year by Zhejiang Machine Product Quality Test Center according to ISO International Standard. |
| --- |
| ITEM | SPECIFICATION |
| Basic Requirement | The surface of the filling machine is glabrous, all powder contact parts are easy to clean and sterilize and invulnerable erode. |
| Electrical System Safety Requirement | Accord |
| Mechanism Movement | Moving smoothly with normal noise. |
| Noisy Requirement | 〈85dB(A) |
| Compression Resistance Test | Accord |
| Insulating Resistance Test | 〉1MΩ |

### YPJ-C Medicine Polisher

The machine is novel professional equipment for pharmacy. Under the drive of continuously variable motor, it can polish and clean the dust attached to the capsule and tablet to improve the surface of medicine polishing.

Main technical data:

- Capacity: 7000 grains/min

- Power supply: 220V  280W

- Dimensions:1150×400×1000mm (Overall)

1300×540×1040 mm (Packing)

- Weight: 45 Kg (Net) 65Kg (Gross)