无锡贝瑞斯机械设备有限公司

WUXI BALANCE MACHINERY EQUIPMENT CO., LTD

Add: D1112, No.158, Wangzhuang Road, Wuxi City, Jiangsu Province, China

Tel: 0086-510-83115339    Fax: 0086-510-83113616    Mobile: 0086-158-616-98920

Skype: platform_balance       MSN: platform_balance@hotmail.com

Email: angela@cnplatform.com            Web: www.cnplatform.com

Contact: Angela Wang

QUOTATION

To: Mr. Kenny                                   Quote No.:

| Fixed Hydraulic Dock Levelers |
| --- |
| Model | Configuration | Quantity |
| DCQ6-0.7 | Rated Capacity (kg) | 6000 | 1 Set |
|  | Acclivity Range (mm) | 400 |  |
|  | Declination Range (mm) | 300 |  |
|  | Self Height (mm) | 600 |  |
|  | Platform Size (mm) | 2500*2000 |  |
|  | Lip plate Dimension (mm) | 400*2000 |  |
|  | Cylinder | Diameter: 80mm (1 Pcs), Diameter: 40mm (1 Pcs) |  |
|  | Motor Power (kw) | 1.5kw |  |
|  | Voltage | 220V/3Ph/50Hz |  |
| FOB SHANGHAI PORT, CHINA ------ US$ 22,260/ SET (Delivery by one LCL with other clients’ products) |

Above includes the following configuration:

| No. | Name | Configuration |
| --- | --- | --- |
| 1 | Material of platform | 6mm antiskidding checkered steel plate |
| 2 | Platform Lip plate | 14mm tablet and 3mm anti-skid checkered steel plate (with curve) |
| 3 | Platform framework | Q345B high strength manganese steel 100*40*4 rectangular tube |
| 4 | Chassis | Q345B high strength manganese steel 8# Chinese standard channel steel |
| 5 | Motor power | 1.5 kw |
| 6 | Voltage | 220V/3 PHASES /50HZ |
| 7 | Appliance | Relay, Contactor, Push Button, etc |
| 8 | Sealing element | Y type rings, O -rings |
| 9 | Hydraulic medium | 32# wear-proof hydraulic medium |
| 10 | Cylinder | Diameter: 80mm (1 Pcs), Diameter: 40mm (1 Pcs) |
| 11 | Auto tire collision rubber pad | 2 pcs (each 100mm thick) |
| 12 | Hydraulic device | Hydraulic device set inside, platform equip electrical control button |
| 13 | high-pressure oil tube | High pressure Double-layer steel wire mesh structure 602-0802-48.0MPa |
| Note: 1. Connecting material: gas shielded arc welding (Hardness higher, use life longer, level higher than normal electric welding) 2. It equips with emergency descending device when power-off, over-load protect device, explosion prevention device |

Summary:

- Terms of validity: 1 month

- Payment: USD 100% paid in advance by T/T.

3. Time of Delivery: 20 working days after receipt of the payment.

4. Warranty: 1 Year.