Quotation Sheet

Quotation No.: SN-Q2013073027                                           Dated: 30th July, 2013

# Submitted To: ООО "НРБТ-СТЕПНОЕ"

Subject: Supply 20T/day Flake Ice Machine With Complete Refrigeration System(R404A)

# Design data

1	Power supply	:	3ph-380V-50hz (±5%)

2	Standard working condition	:     Water temp.25℃，ambient temp.40℃。Applicable condition:ambient temp.5℃-40℃，water temp.0℃-35℃ (fresh water)

Item     Commodities& Description             Qty.           Price

1.     Flake Ice Machine Complete ( F200AF)          1 Unit        USD 63,011.00

- capacity :20T/day

- thickness of flake ice : 1.5-1.8mm

- installation power : 110.5 kw

- water consumption : 0.84m³/hr

- refrigerant :R404A

- overall dimension : 3750x1950x2944mm

- running weight : about 6.5 T

TOTAL  (FOB FUZHOU)                USD 63,011.00

TOTAL SAY    US DOLLAR SIXTY THREE THOUSAND ELEVEN ONLY

# *The price valid for one month, Quote given is on basis of exchange rate: usd=6.15rmb. It is subject to change if the exchange rate varies.

Technical data:

| 1. | 3 Set | Semi hermetic piston compressor unit |
| --- | --- | --- |
|  |  | Compressor Refrigerant capacity Evaporating temperature Condensing temperature Power supply Refrigerant | Bitzer 41.1 -22 43 3Ph,380V,50Hz R404A | 6F-40.2 kw ℃ ℃ |
| 2. | 1 Set | Flake ice evaporator | F200SF Snowkey |
|  |  | The water from external source flows into the water tank where there is a float valve for controlling interior water level. Then water is guided to the upper part of the ice machine body through the line by the pump of the water tank, charged into the water distributing pan through the water supply opening in the upper part and evenly sprinkled onto the inner wall of the evaporator by water distributing pan. The water that doesn’t freeze on the inner wall falls onto the water connecting dish, flows into the guidance trough and then into the water tank for re-circulation. |
| 3. | 1 Set | Air cooled condensor | FJXR-C2-250 Greenhalgh |
| 4. | 1 Set | Oil seperator | Carly |
| 5. | 1 Lot | Refrigeration valves |
|  |  | included all necessary refrigeration parts, including check valve, pressure gauge, pressure controller(high pressure, low pressure, double pressure), liquid sight glass, filter, electromagnetic valve solenoid valve and so on. |
| 6. | 1 Lot | Refrigeration pipe connecting |
|  |  | included all necessary refrigeration pipes, including gas exhaust pipe, gas return pipe, oil pipe, insulated pipe, water pipe and capillary with regulated paint. |
| 7. | 1 Lot | Compressor oil and refrigerant |
|  |  | All compressor oil and system refrigerant will be filled in the system after it is tested and accepted. |
| 8. | 1 Set | Electrical box and control system |
| 9. | 1 Set | Base support frame |

# Terms and Conditions :

- Packing: export worthy package suitable for container transportation.

(2) Delivery time: ready for shipment within 55days after the date of L/C.

(3) Pre-shipment inspection :Supplier’s pre-shipment inspection is Final ;pre-shipment inspection by third Party on buyers cost.

(4) Installation and commissioning :the related fee such as visa, round-trip air tickets, boarding and lodging, traffic of seller’s engineers should be paid by the buyer.

(5) Warranty: One year after commissioning or 18 months from the date of shipment,subject to the early expiry.

(6) Terms of payment: by irrevocable at sight Letter of Credit covering 100% of invoice value in favor of the seller allowing transshipment preferably through our bank:

PAYEE'S BANK:China Construction Bank, Fujian Changle Branch

BANK ADDRESS: Zhenghe Road, Chengguan West District, Changle City, Fujian China

SWIFT CODE: PCBCCNBJFJX

PAYEE'S NAME：FUJIAN SNOWMAN CO.,LTD

PAYEE'S ADDRESS: Binhai Industrial District of Fuzhou, Fujian Province, China.

A/C NO. OF PAYEE: 3501 4614 7002 2010 0362