# QUOTATION

Date: 15-08-2013                                                        Validity of quotation: 1 month

No.:ZYMW20130815

SUBJECT OF QUOTATION

| NO. | NAME OF GOODS | QUANTITY | UNIT PRICE | AMOUNT PRICE |
| --- | --- | --- | --- | --- |
| 1 | ZYYX25-183.3-1100 Tile Roll Forming Machine | 1 SET | USD | USD |
|  | FOB Ningbo |

DELIVERY: The machines will be ready within 60 days from receipt of down payment as well as approval of sales contract, technical scheme and profile drawing. The shipment will be made within 10 days after the seller receives the balance by T/T.

TERMS OF PAYMENT: 30% of the contract amount as down payment; the balance is to be paid by T/T before shipment. Installation charge is to be paid before installation by T/T.

Cost of Installation:

The buyer should pay the installation charges USD1000 for one machine. One technician stays 2 days to install the machine in buyer’s factory. The buyer pays the seller’s technicians travel cost outside China, including round air tickets fee, accommodation and food, provide transportation from living hotel to the work place, necessary communication, and insurance, etc.

WARRANTY: 12 months limited warranty starting from date of delivery, excluding wear parts. Shipping cost for parts to be replaced during warranty period have to be borne by the customer.

Roof Tile Forming Machine

1.Technical parameter

| Item | Specification |
| --- | --- |
| Material | Type | Pre-painted steel coil & galvanized coils |
|  | Thickness(mm) | 0.4-0.6 |
|  | Yield strength(mpa) | 235-345 |
| Roller material | 45#Chrome steel |
| Forming speed(m/min) | About 15-20 |
| Output speed(m/min) | 2-3 |
| Speed adjusting mode | AC Frequency |
| Roller drive | Decelerating motor + Chain drive |
| Cutting mode | Hydraulic cutting |
| Cutter material | Cr12 mould steel |
| Length measurement | Encoder |
| Control mode | Mitsubishi PLC |
| Operating mode | Button + Mitsubishi Touch screen |
| Main motor power(kw) | 5.5KW |
| Total power(kw) | 11KW |

2. Components of machine

| Decoiler | 1set |
| --- | --- |
| Feeding & guiding device | 1set |
| Main roll forming machine | 1set |
| Hydraulic pressing system | 1set |
| Hydraulic cutting system | 1set |
| Controlling system | 1set |
| Run out table | 1set |

3.Process flow:

Decoiler -- Feeding & Guiding -- Roll forming---Hydraulic pressing ---Hydraulic Cutting – product to run out table