Slotting Machine

GYKC300 slotting machine is applied to cut irregular cracks of asphalt and cement pavement to regular slot with special cutters for filling.

Specifications

Engine power     18 KW

Fuel tank         22 L

Cutters number    6

Slotting width     12.5-50 mm

Slotting depth     0-30 mm

Weight           248 kg

Dimensions       950×800×1500 mm

Performance

- Kohler 25HP engine with triple air filter for severe working conditions;

- Imported automatic overload clutch electrical screw with patented technology of stable and reliable performance;

- Various combinations of cutters control slotting width;

- Slotting depth varies from 0-30mm;

- Good materials, innovated structure and specially-processed cutters with National Patent No. ZL200620078489.5;

- Old cutters are still workable with new-replaced cutters, which improve the service efficiency;

- Exclusive crack tracing indicator is able to keep the cutters along irregular cracks.