QUOTATION

We supply LFD-330 Roll Feeding Square Bottom Paper Bag Making Machine, the newest information and quotations as follow:

Ⅰ.Introduction：

we successfully developed the square bottom type of paper bag making machine with roll paper or printed roll paper . This machine features a continuous function of automatic paper suction, gluing, creasing, bottom sticking and bag formation at a stroke.The machine has automatic force controlling machine and the fuction of color marking tracking.All the operation procedures are controlled by PLC,saving laber force.This is an ideal equipment for making paper bag for shopping, loading foods and so on.

Ⅱ. Main Technical Parameter

| Type | LFD-330 |
| --- | --- |
| Paper Roll Width | 550mm -980mm |
| Paper Thickness | 70-140g/㎡ |
| Bag Width | 150-330mm |
| Bag Length | 250-450mm |
| Bottom Size | 80-150mm |
| Speed | 40-80bags/min |
| Total Power | 12Kw |
| Weight of Machine | 8000kg |
| Overall Dimension(LxWxH) | 11000mm×1500mm×1700mm |

Note：

Machine speeds dependent on paper & adhesive qualities, bag dimensions, operator knowledge, and general work philosophy.

Ⅲ. Quotation (F.O.B Ningbo price)

| Model | Price |
| --- | --- |
| LFD-330 | 128000USD |

Our price valid period last for 2 months.

Ⅳ.Delivery

Within 30 days shipment the machine，we manufacture the machine after we receipt 30% deposit.

Payment:100% T/T

Guarantee period: 1 year

Packing: with stretch film and bubble film.

It also can be packing with wooden box (you need to pay the extra fee)