Línea de extrusión de perfil de PVC YF-240

| Objeto: | Dispositivo de extrusión de perfil de PVC YF-240 PVC, molde de acuerdo a los requisitos |
| --- | --- |
| Prueba: | To be run in seller’s factory with our raw materials to finial products. |
| Instalación: | El vendedor va a enviar el ingeniero a la fábrica del comprador después del envío con la confirmación del comprador |
| Garantía: | Un año |

◆Resumen

| 1. | Capacidad: | 4-5 ton / 24h (PVC) |
| --- | --- | --- |
| 2. | Potencia de trabajo de línea de extrusión: | 70KW |
| 3. | Tamaño total de línea de extrusión: | 25M(L) * 2.5M(W) |

Nota:

(1) En general, la mayoría de PVC puede ser conveniente, pero donde se utiliza el material, el tipo del tornillo.

(2) Todas las unidades de medida de la mesa del calibrador está conformado con el estándar del GB. Los equipos enteros tienen garantía de calidad de un año. Después de un año, las guarniciones se suministrará en un precio preferencial.

(3) El vendedor ayudará al comprador a disposición del taller. El vendedor le enviará los técnicos para probar la máquina en el taller del comprador gratis

◆Lista de la máquina extrusora de perfil de PVC

| NO. | Nombre y tipo de la máquina | Cantidad | Comentario |
| --- | --- | --- | --- |
| 1. | Alimentador de resorte | 1 | Transporte y alimentado a los materiales de energía mixta |
| 2. | Máquina extrusora con doble tornillo cónico SJSZ65/132 | 1 | Extrusora principal |
| 3. | Molde de perfil de PVC | 1 | 38CrMoA1A |
| 4. | Tanque de apresto vacío | 1 | enfriamiento y formado |
| 5. | Remolque YF-240 | 1 | Tracción |
| 6. | Cortadora | 1 | Corte fijo |
| 7. | Apilador automático | 1 | Apilado |

◆Machine Specification

1. TS Series Plastic Spring Feeder

| Loading capacity | 150-300KG/H |
| --- | --- |
| Feed box volume | 150 L |
| Motor power | 1.5KW |
| Working angle | 35° |
| Spring Length | 5 meter |
| Stainless steel pipe | Φ 63 ×5m |
| Travel switch | ME8169 |

Note: The above parameters can be customized according to customer's requirements

- SJSZ65/132 Conical Twin Screw Extruder

| No. | Part name | Model and specification |
| --- | --- | --- |
|  |  | SJSZ65/132 | Quan | Remark |
| Capacity: 150kg/h~280kg/h |
| 1 | Screw | Diameter: Φ65/132 Material: 38CrMoA1A, Nitriding Nitriding layer Thickness: 0.4-0.6mm Surface rigidity:740-940HV Surface roughness: Ra ≤0.8um. Speed of Screw: 3-36rpm | 2 | Zhejiang Guangming |
| 2 | Barrel | Material: 38CrMoA1A, Nitriding Nitriding layer Thickness: 0.5-0.7mm Surface rigidity:940-1100HV Surface roughness: Ra ≤0.8um. | 1 | Zhejiang Guangming |
| 3 | Reducer Gearbox | Type: SZ65 horizontal Gear Material: 20CrMoTi, Nitriding, Honing Reducer Motor: WB100-L2D-43 , 0.75kw | 1 | Zhejiang |
| 4 | Distributor Case | Type: SZ65 Gear Material: 38CrMoA1A, Nitriding Axis Material: 40Cr Main Bearing: Wafangdian Bearing | 1 | Wuxi Senjie |
| 5 | Exhaust system | Water loop vacuum pump Motor: SZ-0.5, 1.5KW Vacuum degree: -0.08Mpa | 1 | Ningbo / Joint veture |
| 6 | Main driving motor | Y250L-4 , 37kw | 1 | Suzhou Deneng |
| 7 | Main AC inverter | 3G3RV-ZV1 , 37kw | 1 | Yaskawa(Japan) |
| 8 | Feeder AC inverter | VFD-007B , 0.75kw | 1 | Yaskawa(Japan) |
| 9 | Barrel heating method | 11 heating zones, Foundry Aluminum heating coil with the stainless steel shroud outside, 24kw | 4 | Jiangsu |
| 10 | Barrel cooling fan | DF4 , 2pcs 0.25kw, 1pc 0.37KW | 3 | Wuxi / S |
| 11 | Temperature control meter | E5EZ-R3 | 10 | OMRON (Japan) |
| 12 | thermocouple | K | 10 | Zhejiang |
| 13 | Tachometer | SX6 | 2 | Taiwan |
| 14 | Ampere meter | SX6 | 2 | Taiwan |
| 15 | General power air switch | DZ10-250A | 1 | Zhejiang zhengtai |
| 16 | Other air switch | 1P 2P 3P DE47-63 | 1 | Zhejiang zhengtai |
| 17 | Contactor | LC1 | 1 | Schneider (France) |
| 18 | Intermediate relay | HH54P | 1 | Fuji (Japan ) |
| 19 | Button, Indicator light | LAY | 1 | Schneider (France) |
| 20 | Axial-flow fan | YD150 | 1 | Jiangsu |
| 21 | Aviation plug | 16A | 7 | Suzhou yida |
| 22 | Aviation plug | WP2030A-2P | 6 | Weipu |
| 23 | Alarm system | Infrared monitor | 1 | Imported |
| 25 | Oil circulating system |  | 1 | Fangli |

- PVC Profile Mould & Die

| Mould Material | 38CrMoA1A |
| --- | --- |
| Inner Face | Hard chrome plating |

- Vacuum sizing tank

| 6meter length, Stainless steel, Manual thread adjustment with leveling device,30pcs cooling pipe joints, 30pcs vacuum joints, water consumption:7m3/h |
| --- |
| No. | Part name | Model and specification | Quan | Remark |
| 1 | AC contactor | D1810,1210, 0910 | 9 | Schneider(France) |
| 2 | Thermal overload relay | 10-16A 1316 | 4 | Schneider(France) |
| 3 | Thermal overload relay | 1314 6.3-10A | 2 | Schneider(France) |
| 4 | Thermal overload relay | 1312 4.5-6A | 2 | Schneider(France) |
| 5 | Thermal overload relay | 1308 2.5-4A | 1 | Schneider(France) |
| 6 | Circuit breaker | DZ47-63 3P100A | 1 | Zhejiang zhengai |
| 7 | Start button with light | LA39-10D/g31 | 9 | Shanghai ergong |
| 8 | Stop button | LA39-11 red | 8 | Shanghai ergong |
| 9 | Emergency stop button | LA39A-11Z/r | 1 | Shanghai ergong |
| 10 | Speed meter counter | UP5135 | 1 | shenzhen |
| 11 | Potentiometer | WXD3-13 10k | 1 | changzhou |
| 12 | Travel switch | LXK3-20s/p | 1 | shanghai |
| 13 | Lifting reducer | WP wk60 20:1 | 4 | zhejiang |
| 14 | Vacuum pump | SZ-3A 5.5kw | 4 | Zhejiang/ Taiwan |
| 15 | Walking motor | WP wk60 30:1 | 1 | zhejiang |
| 16 | Water pump | 2BL-6 1.5kw | 1 | Joint-venture |
| 17 | Draught fan | XGB-3 1.1kw | 1 | wuxi |

- YF-240 Haul-off

| YF-240 type, Traction:4KN, rate:1～5m/min, The effective length of chain: 2.2m, Air pressure: 0.5-0.7Mpa, Attached with another film laminator. |
| --- |
| No. | Part name | Model and specification | Quan | Remark |
| 1 | AC relay | 0901 | 2 | Schneider (France) |
| 2 | Intermediate relay | HH54P | 1 | Schneider (France) |
| 3 | Transducer | 3G3JV 3.7kw | 1 | YASKAMA (Janpan) |
| 4 | Traction motor | SKTH44C 1.5kw | 2 | zhejiang |
| 5 | Chain | 16A | 4 | jiangsu |
| 6 | Air cylinder | XQGB160×140-CB | 2 | Taiwan Airtac |
| 7 | Air cylinder | XQGB50×100-CB | 1 | Taiwan Airtac |

- Cutter

| Cutting motor:2.2kw, Rotating speed: 2860r/min. Cutter with SiC blade, diameter is 400mm, air pressure : 0.5-0.7Mpa. It is controlled by time relay, which can work stable and be adjusted easily without repair. |
| --- |
| No. | Part name | Model and specification | Quan | Remark |
| 1 | Cutting motor | Y100L-2 2.2kw | 1 | Wuxi longxin |
| 2 | Air cylinder | XQGB50×175GB | 1 | Taiwan Airtac |
| 3 | Air cylinder | XQGB50×500 | 1 | Taiwan Airtac |
| 4 | Magnetic valve | 6102 | 2 | Taiwan Airtac |
| 5 | Fast purge valve | QE-03 | 1 | Zhejiang ningbo |
| 6 | One-way chock valve | ASC200 | 1 | Zhejiang ningbo |
| 7 | Pressure reducing valve | AR2000 | 3 | Zhejiang ningbo |
| 8 | Circuit breaker | DZ47-60 2p 20A | 2 | Zhejiang zhengtai |
| 9 | Circuit breaker | DZ47-60 2p 5A | 1 | Zhejiang zhengtai |
| 10 | Indicator light | AD16-22D | 2 | Shanghai ergong |
| 11 | On (button) | LA39-11 green | 2 | Shanghai ergong |
| 12 | Off (button) | LA39-11 red | 1 | Shanghai ergong |
| 13 | Emergency stop button | LA39A-11Z | 2 | Shanghai ergong |

- Automatic stacker

| 6 meter Length, stainless steel, Automatically air operated turning |
| --- |
| No. | Part name | Model and specification | Quan | Remark |
| 1 | Air cylinder | 50×100GB | 2 | Taiwan Airtac |
| 2 | Magnetic valve | 6102 | 1 | Taiwan Airtac |
| 3 | Travel switch | LXK3-20s/p | 1 | Shanghai |

WUXI SENJIE PLASTIC MACHINERY CO., LTD

Address: NO.61 Renmin East Road, Yangshi Luoshe Town, Wuxi City, Jiangsu, China.

Tel: 0086-510-8021 9119   Mobile: 0086 13915229945   Fax: 0086-510-8021 9159

Attn: Sherry Wang   E-mail: wxsenjie@gmail.com  Website: www.sjsjcn.