200A Oil Press machine

This machine is suitable for the extraction of vegetable oils from such oil-bearing materials as rape seed, peanuts, sesame seed, cotton seed, Soya beans, coconuts, tea seed, sunflower seed, etc. (The pressing worms can be replaced as required by the user for the purpose of the extraction of oils from some other oil-bearing materials, such as rice bran oil and the like.).

Technical data:

1、Capacity (The treating capacity for seeds)

| Name of oil seed | Capacity （kg/24h） | （%）Oil yield | （%）Residual oil in dry cake |
| --- | --- | --- | --- |
| Rape seed | 9000～10000 | 33～38 | 6～7 |
| Peanuts | 9000～10000 | 38～45 | 5～6 |
| Sesame seed | 6500～7500 | 42～47 | 7～7.5 |
| Cotton seed | 9000～10000 | 30～33 | 5～6 |
| Soya beans | 8000～9000 | 11～14 | 5～6 |
| Sunflower seed | 7000～8000 | 22～25 | 8～9.5 |
| Rice bran | 10000-12000 | 10～14 | 7～8 |

2、Inside diameter of steaming kettle：     φ1220 mm；

3、Stirring shaft speed：                 35 rpm；

4、Steam pressure：                     5～6 kg/cm2；

5、Pressing bores：   Front section   φ180 mm；   Rear section   φ152 mm；

6、Pressing worm speed：                    8 rpm；

7、Feed shaft speed：                     69 rpm；

8、Pressing time in cape：              2.5 min；

9、Seed steaming and roasting time：    90 min；

10、Max. temperature for seed steaming and roasting：125-128 ℃；

11、Power demand：                          18.5 kw；

12、Overall dimensions (L×W×H)： 2850×1850×3270mm；

13、Weight：                                     5000 kg

*  All such main parts of this machine as worm shaft, pressing worms, cage bars, gears and so forth are made of high-grade alloy steel through hardening treatment. As a result, in spite of the conditions of high temperature and abrasion under which they work day and night, they keep durable for a considerable period.

*  The combination of steaming and roasting is also one of the features of this machine. It can be regulated in accordance with the varied requirements of various oil-bearing materials for the temperatures before pressing so as to get high quality oils.

*  The whole process from feeding, steaming, roasting up to the discharge of oil and cake goes, on automatically and continuously, so it is easy to operate the machine, which results in the saving of labour.

Heating Mode: Steam

1. Inside Diameter of Steam Boiler: ø 1220mm,
2. Steam Pressure: 5~6 kg/cm2,
3. Max.Temperature for Seeds Steaming and Roasting: 110~128℃,

Oil press machine Price: USD 10,950.00 /Unit,

FOB Shanghai，China, with motor, packing

Delivery: 7~10 days after receiving down payment

Valid : One month

- Payment term

1) If the amount is less than USD 10,000, 100% prepayment by T/T

2) If the amount is more than USD 10,000, 30% as prepayment by T/T, the balance of

70% before loading

- Quality Guarantee Terms

Quality guarantee term is for one year. Any broken which are caused by machine-self and

quality will be responsible for our manufacturer. Others which are caused by operation

mistakes, man-made problems, etc will be responsible for clients-self.

- Electricity situation

All of the machines listed above are matched Chinese Standard electricity situation:

380 Volts, 50Hz, 3 phases. If clients have special electricity requirements on the machines, clients should pay the extra cost of electricity special require.

If you have any question or advice , pls feel free to contact us without any hesitation .

Thanks and regards