Computer Control Two-layer Rolling Bag-making Machine

for Vest & Flat Bags  DZB-500/600/700/800

Characteristics:

This machine, a specially-designed point-cut rolling dual-purpose one  for vest & flat bags, is controlled by a computer. The step(servo) setting length  system reduces the  sealing-cutting  dimensions errors, and the  installation of photoelectric eyes track help make the position of figure of  printing  bags  accurate.

The  computer  numerical control can be selected  to adjust  the  length of  bag. The machine  will automatically stop and sound a warning if there is something wrong with the printing bags.

| Model | DZB-500 | DZB-600 | DZB-700 | DZB-800 |
| --- | --- | --- | --- | --- |
| Max Width | 400mm | 500mm | 600mm | 700mm |
| Max Length | 1200mm | 1200mm | 1200mm | 1200mm |
| Bag-making Thickness | 0.008-0.10mm | 0.008-0.10mm | 0.008-0.10mm | 0.008-0.10mm |
| Speed per Minute | 40-120pcs/min | 40-120pcs/min | 40-120pcs/min | 40-120pcs/min |
| Power Motor | 1.1kw | 1.1kw | 1.5kw | 1.5kw |
| Electric heating Power | 1.2kw | 1.6kw | 2kw | 2.2kw |
| Weight of Machine | 800kg | 850kg | 900kg | 1000kg |
| Machinery Dimensions(L*W*H) | 3300X1100X1500mm | 3300X1200X1500mm | 3300X1300X1500mm | 3300X1400X1500mm |
| Packing Dimensions(L*W*H) | 3400X1200X1700mm | 3400X1300X1700mm | 3400X1400X1700mm | 3400X1500X1700mm |

XY-FB45/55 Mini Film Blowing Machine

Use:

The cylinders and screws of the extruder are made of high quality alloy steel with optimum hardness and strong corrosion resistance after nitrogen

treatment and precision finishing, The screw with specially designed will facilitate the producing capacity and plasticizing. It is applied to blowing

the plastic films like LDPE. LLDPE. It is widely used in producing packing bags for food, cloth, rubbish and vest.

| Model | XY-FB45 | XY-FB50 | XY-FB55 |
| --- | --- | --- | --- |
| Screw Diameter | 45mm | 50mm | 55mm |
| Screw Ratio | L/D28:1 | L/D28:1 | L/D28:1 |
| Screw speed | 10-100r/min | 10-100r/min | 10-100r/min |
| Power of Main Motor | 7.5KW | 11KW | 15KW |
| Main Output | 30kg/h | 35kg/h | 45kg/h |
| Single-sided Thickness of Film | 500mm | 600mm | 800mm |
| Max. Folding Width of Film | 0.006-0.10mm | 0.006-0.10mm | 0.006-0.10mm |
| Total Power | 19Kw | 22Kw | 25Kw |
| Overall Dimensions | 1300kg | 1400kg | 16000kg |
| Weight of Machine | 4800x2200x4200mm | 4800x2200x4200mm | 4800x2200x4200mm |

Xinye( E-light) Packaging Machine Factory

Add: New No.104 Main Roadside, Yongguang, Shangwang, Ruian, Zhejiang, China

Mobile: 0086-13967703011      Fax: 0086-577-65132727

Website: www.raxinye.com     Email: xinye3@cnxinye.cn