产品规格书

Product  Specifications

产品名称：     600x600-30W面板灯

产品型号：       JY-P66-30W-A

版 本 号：             1.0

页    数：           共9页

注：规格若有变更或其中产品停产，恕不另行通知，请在订购之前向我公司销售代表或产品工程师咨询。(Attention:  any  change  to  specification  or  stop of production  will 	not   be   notified accordingly.   Kindly   please   consult   with   sale representatives in our  factory  before  order)

- 产品概述  (General description)

LED面板灯是一款宜美高档的室内照明灯具，用来替代现有传统的面板照明灯具。其外边框由铝合金经阳极氧化而成，不仅防生锈，同时使得整个灯具设计美观简洁、大气豪华。LED面板灯设计独特，光经过高透光率的导光板后形成一种均匀的平面发光效果，照度均匀性好、光线柔和、舒适而不失明亮，可有效缓解眼疲劳。

Joywin LED panel light is an elegant and high-classic indoor luminaire used to replace existing halogen panel light. The edges made of aluminum are oxidated to be anti-rust and to enhance the grace of its appearance. The light guiding plate made of fire-proof PMMA material makes the light distribute evenly without glare, protecting the eye-sight with soft light.

二. 产品特性(product features)

- 光源采用节能绿色环保的小功率高亮度 SMD 光源，无紫外线、红外线、热辐射和汞污。

Utilizing green, eco-friendly, low power SMD LED without UV and IR emission, heat radiation and mercury pollution.

- 节能效率高。比白炽灯节能 90%，比节能灯更节能 60% 。

High efficiency in energy saving, can save up to 90% energy compared with incandescent bulb and 60% compared with CFL.

- 经特殊工艺封装,坚固耐用，寿命可达 50000 小时。

Encapsulation by special craft, which is characterized by solidity, durability and

long lifetime over 50,000  hours.

- 作为冷光源，LED 灯光不会使物品因照射产生褪色现象。

As cold light source, LED light will not make the color of object fade because of

exposure to light.

- 采用优良材料，做工精细，具有耐高温、高强度、耐腐蚀等优点。

The excellent material, fine workmanship make the LED bulb high-temperature

resistant, high intensity, and anti-corrosion.

- 显色指数高，显示最直观、清晰，且色温可选。

High color rendering index, can clearly light up objects in the most direct way, with

several CCTs available for option.

- 响应快，无频闪、眩光，点亮后瞬间达到全光通量输出。

Instant on, no flash, no glare, reaching to full luminous output constantly after turned on.

- 固体光源，抗震性强，便于运输及安装,安全性高。

Solid-state light source, strong anti-shock and easy to be installed and delivered with high safety .

- 发光方向性强，易于控制光线，有效提高照明系统的效率。

Flexibility of light direction ,  easy control of beams,  increasing  efficiency  of

lighting  system effectively.

⒑	造型优雅、精致、美观、结构简单可靠，紧贴客户需求及感受，融入更多科技元素

及人性化设计。

Elegant, sophisticated, good-looking appearance, simple and reliable structure,

close to the customers' needs and feelings，with more user-friendly design elements

and technology.

三.应用领域 Area of Application

适用于酒店、酒吧、西餐厅、咖啡厅、居家室内装饰等室内照明，可以直接替代原有的普通荧光灯，且其亮度更高。

Suitable for indoor use in hotel、bar、restaurant、coffee house、living room or somewhere indoor that needs energy-saving lighting and high colour rendering index.

四.实物图(Pictures)

五.外形尺寸图  (dimensional drawing)

六. 配光曲线(Light distribution curve)

600x600-30W面板灯配光曲线图

600x600-30W面板灯有效平均照度图

七.产品参数(Product parameter)

600x600-30W面板灯技术参数

| LED Light Number: LED灯具编号： | JY-P66-30W-A |
| --- | --- |
| Input Voltage: 输入电压: | 220 AC 220V 伏特 交流 |
| Polarity: 极性： | Bipolar Protection 双极性保护 |
| Efficiency: 效率： | ≥70% |
| Input Power: 输入功率： | 30W |
| Luminous Output: 输出光通量： | 2100±200 lm |
| Color Rendering Index: 显色指数： | ≥75 |
| Total Size: 总尺寸： | 600x600x9m 600 x600x13.5m |
| Light Source: 灯具使用光源： | SMD 2835 |
| Operating Temperature: 工作温度： | -20~+40 Degrees Celsius -20~+40摄氏度 |
| Storage Temperature: 储藏温度： | -30~+60 Degrees Celsius -30~+60摄氏度 |
| Correlated Color Temperature: 相关色温： | 正白6000K±500K 自然白4200K±500K 暖白3000K±300K |
| Colour： | aluminum colour 铝本色 |
| LED’S Operating Life: 光源工作寿命： | 50000 Hours 50000 小时 |
| Weight: 重量： | 2950±20g 2950±20克 |

八. 安装说明(installation instruction)

九.包装方式(package)

白盒包装

white box packaging

十.保养方法(maintenance)

1.  为了保持灯具的明亮照明效果，请定期（半年一次）进行清洁。灯具不洁处擦拭时，请用柔软布料粘肥皂水拧干后擦拭，再用干布擦净。

In order to keep optimum performance ,please clean  the  product  regularly (recommended  twice  a  year) 。 When  cleaning  the product, please use soft cotton cloth only.

2.  请不要使用香蕉水等挥发性物质擦拭灯具表面，请不要对灯具喷洒任何化学药剂，否则灯具可能会变色或损坏。

Do not use chemical solvents to clean the luminaire, it might damage the surface.

十一.注意事项(Caution)

1. 额定电压是 AC 220V 频率 50/60Hz。在电压过高或过低的状态下长期使用，会影响正常使用的功能和寿命；

As rated voltage is AC  220V 50/60Hz, any operation under high or low voltage for long time will affect the lamp function and early failure.

2. 不可安装在可燃物体内使用，无论什么情况下，灯具不能被隔热衬垫或类似材料盖住；The LED lamp is not allowed in any case to be installed in flammable object and covered by insulation blanket or similar materials.

3. 安装和更换灯时，必须切断电源，保证人身安全；

Before installation and replacement of light, power must be cut off to avoid electric shock).

4.	LED 灯泡不宜用作调光照明场所下使用；

Non-dimmable bulbs are no allowed to be used in dimmers..

- LED 灯泡不能用光学仪器直接观看，等级为 1M；

The LED bulb cannot be seen directly by optical instrument with degree of 1M.

- 当发现灯工作异常（自熄、闪烁）时，请检查电源电压是否正常,如果都正常故障

仍未排除，需调换新灯；

Any abnormal problems (flashing or no light-up) found in the lamp, pls check whether

the power is normal; If yes, then replace the lamp.

- 禁止在室外和雨水淋到的地方使用；

prohibition to be used outdoor or in any place where rain drop.

- 灯具应由有资格的电工安装，接线符合 IEE 电气标准或国家标准；

The luminaire shall beinstalled by a qualified electrician and wired in accordance with the latest IEE electrical regulations or the national requirements.