Quotation

Of

Compulsory Asphalt Batching Plant

QUOTED BY: Mr.Martin Wu

Quotation Date:  Apr. 1st, 2013

Уважаемые дамы и господа :

Спасибо за Ваш запрос. Мы рады представить следующее предложение.

1.	Рамки коммерческого предложения

Рамки коммерческого предложения асфальтобетоносмесительной установки QLB60 указаны в приложении. Ввиду научно-технического прогресса, мы оставляем за собой право обновления.

2.	Срок поставки

Товары будут готовы к отгрузке в течение 30 рабочих дней с завода в г. QuanZhou после технического подтверждения и получения обязательного заказа и предоплаты. Дата подтверждается после получения заказа.

3.	Цена

4.  Установка

Продавец должен отправить инженеров для установки. Все расходы на проживание и питание инженеров за границу (включая расходы на проезд за границу) несет на себя покупатель. Более того, покупатель должен платить инженерам зарплату 60USD в день.

5.	Условия платежа

30% предоплата T/T, 70% оплачивается T/T, когда товар готов к отгрузке.

6.	Срок действия

Данное предложение действует в течение 30 дней с даты предложения указанного на сопроводительном письме.

Appendix I: QLB60 Compulsory Asphalt Batching Plant Main parameters

| Model | QLB(Y)-60 |
| --- | --- |
| Capacity（t/h) | 60 |
| Toal Power (Kw) | 195 |
| Fuel Oil Consumption(Kg/t) | ≤7.5kg |
| Fuel Coal Consumption(Kg/t) | ≤15kg |
| Finished Products Temperature(℃） | 120-160 |
| Aggregate Accuracy | ±0.5% |
| Bitumen Accuracy | ±0.2% |
| Cement Accuracy | ±0.3% |
| Asphalt Contrast | ±0.3% |
| Constant Temperature Accuracy(℃） | ±5 |

Appendix II: QLB60 Compulsory Asphalt Batching Plant Specification

| NO. | Name | Configuration | Specification | QTY | Unit | Manufacturers | Image |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Aggregate Feeding System | aggregate hopper | 5.5m3 | 3 | pc |  |  |
|  |  | opening device |  | 6 | set |  |  |
|  |  | weighting hopper |  | 1 | set |  |  |
|  |  | roller | φ320 | 1 | pc |  |  |
|  |  | tension device |  | 1 | set |  |  |
|  |  | cleaner |  | 1 | set |  |  |
|  |  | flat belt | B650*17900*10 | 1 | pc | Shandong Laizhou |  |
|  |  | electric roller | JBT7.5-1.25-400*650 | 1 | set | Jiangsu |  |
|  |  | cylinder | QGB-ES80*200-L3 | 6 | pc | Airtac |  |
|  |  | weighing sensor | CST2000Kg | 4 | pc | Transcell |  |
| 2 | Burning System (Two sets) | burner |  | 2 | pc |  |  |
|  |  | centrifugal fan | 9-19No5.6A right180° | 2 | set | Fujian East Asia blower |  |
|  |  | fan motor | Y160M1-2；N=11kw | 2 | set | Jiangsu dazhong |  |
|  |  | diesel oil gear pump | GC-32 | 2 | set | Fujian Quanzhou |  |
|  |  | motor | Y100L1-4；N=2.2kW | 2 | set | Jiangsu dazhong |  |
|  |  | fire-resistant brick |  | 2 | set | Xinghua |  |
|  |  | autoigniter | PQCI-30A | 2 | set | Changsha xinxing |  |
| 3 | Drying Roller System(Two sets) | drying roller |  | 2 | set |  |  |
|  |  | big gear loop |  | 2 | pc |  |  |
|  |  | decelerate case | ZQ350-8.23-1 | 2 | set | Jiangsu |  |
|  |  | motor | Y160M-4；N=11kW | 2 | set | Jiangsu dazhong |  |
|  |  | seal loop |  | 4 | set |  |  |
|  |  | frame |  | 2 | set |  |  |
| 4 | Cold Aggregate lifting system(Two sets) | Cold Aggregate lifting hopper | 1.1M3 | 2 | set |  |  |
|  |  | Aggregate lifting rack |  | 2 | set |  |  |
|  |  | windlass | BWY27-29-7.5kw | 2 | set | Jiangsu |  |
|  |  | feeding hopper |  | 2 | pc |  |  |
| 5 | Hot Aggregate lifting system | Hot Aggregate lifting hopper | 1.1M3 | 1 | set |  |  |
|  |  | Aggregate lifting rack |  | 1 | set |  |  |
|  |  | windlass | BWY27-29-7.5kw | 1 | set | Jiangsu |  |
|  |  | finished material storage hopper | 9ton | 1 | set |  |  |
|  |  | rack |  | 1 | set |  |  |
| 6 | De-dust System | cyclone de-dust device |  | 1 | set |  |  |
|  |  | De-dust pipe |  | 1 | set |  |  |
|  |  | boiler induced-draft fan | Y5-47No8C,right180° | 1 | set | Fujian East Asia blower |  |
|  |  | motor | Y180L-4；N=22kW | 1 | set | Jiangsu dazhong |  |
| 7 | Mixing system | mixer | JS1000 | 1 | set |  |  |
|  |  | cycloid needle wheel decelerate device | XWD8-17-18.5kw | 2 | set | Jiangsu |  |
|  |  | cylinder | QGB-EZ125×250-L3 | 2 | pc | Airtac |  |
|  |  | Discharge hopper |  | 1 | set |  |  |
|  |  | Mixer cover |  | 1 | set |  |  |
| 8 | Powder Weighing System | screw conveyer | LSY219-6M | 1 | pc |  |  |
|  |  | cycloid needle wheel decelerate device | XLDY7.5-5-9 | 1 | set | Jiangsu |  |
|  |  | powder hopper and frame |  | 1 | set |  |  |
|  |  | sensor | CST250Kg | 1 | pc | Transcell |  |
|  |  | cylinder | QGB-ES80×250-L3 | 1 | pc | Airtac |  |
| 9 | Asphalt Weighing System | bitumen weighing tank and frame |  | 1 | set |  |  |
|  |  | sensor | CST250Kg | 1 | pc | Transcell |  |
|  |  | cylinder | QGB-ES80×200-L3 | 1 | pc | Airtac |  |
|  |  | Cylinder | QGB-ES80×160-L3 |  | pc | Airtac |  |
|  |  | gear bitumen pump | CLB100 | 1 | set | Xinjin |  |
|  |  | motor | Y112M-4,N=4kW | 1 | set | Jiangsu dazhong |  |
|  |  | revolving plug valve | X44W-16C,Φ40 | 1 | set |  |  |
| 10 | Frame | mainframe |  | 2 | set |  |  |
|  |  | platform、railing |  | 1 | set |  |  |
|  |  | Traction frame |  | 2 | set |  |  |
|  |  | Front axle | 7.50-20 | 1 | set |  |  |
|  |  | Rear axle | 8.25-12 | 2 | set |  |  |
|  |  | supporting leg |  | 12 | pc |  |  |
| 11 | Electronic Control System | control room |  | 1 | pc |  |  |
|  |  | 1P air condition |  | 1 | set | Domestic brand |  |
|  |  | control platform | include computer system | 1 | pc |  |  |
|  |  | touch screen | eview | 1 | set | Taiwan |  |
|  |  | switch |  | 6 | pc | OMRON |  |
|  |  | connect cable |  | 1 | set |  |  |
| 12 | Pneumatic System | air compressor | W-0.9/7-E；N=7.5kW | 1 | set | Fujian jianyang |  |
|  |  | pneumatic system central parts |  | 1 | set |  |  |
|  |  | FRL Combination | QFLJWA-L15 | 1 | pc | Airtac |  |
|  |  | electromagnetic valve | Q25DC-L15 | 7 | pc | Airtac |  |
| 13 | Coal grinding equipment | Coal grinding mill | MPF600 | 1 | set | Fuzhou huayi |  |
|  |  | Motor | N=22kw | 1 | set | Fujian mindong |  |
|  |  | Coal handling pipe |  | 1 | pc |  |  |
|  |  | Control cabinet |  | 1 | pc |  |  |

EXCLUSIONS

a)	Civil works, but provide loading drawing.

b)	Any power source.

c)	Link cables between generating set and our motor control panel and essential services panel.

d)	Any item not definitely specified.