| Modelo | STNDP-801AB3 | HSGP-4KB |
| --- | --- | --- |
| Tamaño máximo de grabado (mm) | 300*200*100mm | 300*400*150mm |
| Ancho de pulso | ≤6ns (1) |  |
| Velocidad del grabado | máximo :3000 puntos/s; normal:2800 puntos / s (2) | máximo : 4000 puntos /s, normal:？ |
| Diámetro de un punto | 20-40μm | 20μm |
| Precisión de localización repetida | ＜10μm (3) | 10μm |
| Tiempo de trabajo continuo | >24 horas | >24 horas |
| Max DPI | 600DPI (4) | 800DPI |
| Enfriamiento | air | air |
| Diodo láser de vida del módulo | ＞12000 horas ( Es un parámetro actural verdadero ofrecido por EE.UU. empresa coherente ) | 20000 horas or 25000 horas? (5) |
| Consumo de energía | ＜800W (6) | 1500W |
| Conexión eléctrica | Solo 220V or 110V (+/-10%); 50Hz or 60Hz |  |
| Caso típico de la velocidad normal de grabado | tamaño del cristal ：50*80*50mm patrón ：300000 puntos tiempo de grabado ：＜2 acta |  |
| Garantía | 2 año (1 años de diodo ) (7) | 1 año |
| Exigencias de funcionamiento | temperatura de la habitación :5--35℃; humedad de la habitación :＜70% sin condensación | temperatura de la habitación :15-30℃ |
| Peso | 110Kg |  |
| Tamaño de la máquina (L*W*H)(mm) | 760*660*760 (32.3''X26''X30.7'') |  |
| Tamaño del paquete (L*W*H)(mm) | 1120x760x1040 |  |

STNDP-801AB3 y HSGP-4KB

PS: place which marked as(1)(2)(3)…… will be interpreted below the table. Pls check!!!

1).Smallest pulse width in the market (≤6ns), to make the highest peak power laser have the good adaptability for different crystals on different rigidity,

machines with a pulse width biger than 6 ns will ask the top grade K9 crystal (soft material), which price is higher;

2) Engraving Speed: 3000 dots/s is the max engraving speed, and normal is 2800 dots/s, HSGP-4KB’s max speed is 4000 dots/s, and how is the normal speed, I think you need to comfirm this parameter, as we know machines are always work as normal speed but not max speed;

3)Good repeated location accuracy <10μm: this good ability to make sure the engraved image more nice. For this value, the smaller, the better;

4) Authentic Max DPI (600DPI): about the DPI of the machines, it's a parameter to tell you how many dots in one inch, and our machine with smallest size in the market, the diameter of our engraved points is 20μm,on this sizes, the actural dpi counted as below:

1 inch=2.54cm, and our point size is 20-40μm, 1mm=1000μm, so the max DPI is 2.54x10x1000/20=1270, but this not includes the point distance when engrave images, so usually the DPI is half,about 600 DPI, though in the market, some machine wrote the DPI is 800, but if you account it like this way, you will found that value is unauthentic);

5) Life time of laser diode (>12000 hours, usually can up to 18000 hours): We impoerted the diode laser module from USA Coherent, and the supplier offer us the lifetime, so we offer it to customers, it is a real actural parameter. HSGP-4KB: as shown in the Chinese version homepage which is 20000 hours and in English version which is up to 25000 hours, maybe you need to confirm with them again to get an authentic parameter;

6) Our machines' power is less than 800w, it is a low power consumption and non-polluting machine;

7) 2 years' warranty: we designed our laser box-key part of the 3d laser machine by ourself (Key part imported abroad), we have the good technology to make the products according to customers' request. And as the laser technology is ours, so we have the confidence to offer the 2 years' warranty to all our machines.