TELÃO LED SMD PARA O USO DE ALUGUEL de HTS

Pixel de 4mm, telão LED fino de alumínio fundido

P4

O sistema de telão LED premium de alumínio fundido 4mm para uso interno.

Montagem rápida sem costura, excelente qualidade de imagem, amplo ângulo de visão e confiabilidade incomparável.

Características:

- A espessura de gabinete é apenas 75mm, o peso de gabinete é apenas 9.5 kgds/tile.

- Diferentes opções de cor da tampa traseira de acordo com os requisitos dos clientes.

- Circuito integrado de driver 16 bit com cores ricas e delicadas, taxa de atualização de 3500Hz.

- Bloqueio de suspensão rotativo e botão de segurança manual para evitar a caida de paineis.

- Design especial da tampa traseira permite diferentes formas de manutenção.

- Adota a carcaça de alumínio fundido para garantir a planeza do telão e sem costura entre os telões.

- Usa os conetores de Neutrik, rápida montagem, durável.

- Adota os ventiladores de refrigeração de DC, menos ruido para o uso interno.

- Suporta a instalação do tipo de suspensão e empilhamento, adequado para ambos formas de instalação fixa e as atividades de aluguel.

FOTOS DE GABINETE P4

VISTA DIANTEIRA DE GABINETE

VISTA TRASEIRA DE GABINETE

Technical specification

| Model | P4 |
| --- | --- |
| Pixel pitch | 4mm |
| Pixel configuration | 1R1G1B |
| LED type | SMD2020 |
| Module size | 256x256mm |
| Module resolution | 64x64 |
| Cabinet resolution | 128x128 |
| Cabinet size | 512x512mm |
| Density | 62500dots/㎡ |
| Brightness | ≥1200 NIT |
| Scan method | 1/16 |
| Best view distance | ≥4m |
| Max. power consumption | 300W/panel |
| Ave. power consumption | 180W/panel |
| Cabinet Weight | 9.5Kg |
| Grey scale | 16 bit、65536 step |
| Color | 281 billion |
| Refresh rate | ≥960 Hz |
| Best view | Vertical: 120°, Horizontal: 120° |
| Color temp | 7500K |
| Frame frequency | ≥60Hz |
| Out of control pixel rate | <1/10000 |
| MTBF | >5000 hours |
| Lifespan | 50000 hours |
| Signal input source | Composite, S-video, Component, VGA, DVI, HDMI, SDI, HD-SDI |
| Working voltage | AC 110/220v 50-60Hz |
| Control distance | Ethernet cable: 100m, Multi-mode optical fiber: 500m, Singel-mode optical fiber: 20km |
| Operation temperature | -20 to +40 |
| Working humidity | 10% to 80% |
| Protection level | indoor |

P4  SYSTEM CONNECTION DIAGRAM