# Предложение

Дата: 25-10-2013                                                                       Срок действия предложения: 1 месяц

## Тема предложения

No.ZYJ20131025-S

| NO. | Наименование товара | количество | Цена за единицу | Общая цена |
| --- | --- | --- | --- | --- |
| 1 | Профилегибочная машина для производства сигма профилей | 1 штук | USD57000 | USD57000 |
|  | FOB Нинбо |

Доставки: Машины будут готовы в течение 80 дней с момента получения аванса, а также
утверждении договора купли-продажи, техническая схема и чертеж профиля. Отгрузка будет производиться за 10 дней после того как продавец получит баланс по T / T.

Условия платежа: 30% от суммы контракта в качестве аванса оплачивается по T / T; 70% баланса должно быть оплачено по T / T до поставки. Сбор упаковки должен быть оплачен до установки по T / T.

Гарантия: гарантия на 12 месяцев начиная с даты поставки, кроме быстроизназиваюшихся деталей.

Стоимость доставки для сменных деталей в течение гарантийного срока должны оплачиваться заказчиком.

Стоимость установки:

Покупатель должен оплатить расходы по установке(USD 100/человек/день). На счет Продавца в указанный счет по T / T перед тем, как техники продавца приехать на завод покупателя. Покупатель оплачивает продавцу стоимости путешествия техников за пределами Китая, в том числе круглые стоимости авиабилетов, проживание и питание, обеспечить перевозки из отеля к месту работы, необходимые коммуникации, и страхование,и т.д.

- Дргие условия: Во вложении технический вариант, проверьте, пожалуйста.

TECHNICAL SCHEME

- NAME OF GOODS: Sigma Roll forming machine

- PROFILE:

- MATERIAL:

1) Suitable Raw Materials: galvanized steel sheet

2)Thickness: 1.5-3.0mm

3) Coil width: as per profile drawing.

4) Yield strength of raw material: Q235

- MACHINE COMPONENTS:

1) Manual decoiler:                 1 set（Capacity : 3 tons）

2) Roll-Forming M/C:               1 set

3) Leveling device:                 1 set

4) Hydraulic Punching:              1 set

5) Hydraulic Cutting:                1 set (3 Pieces of cutting blade)

6) Hydraulic station:                 1 set

7) PLC Control System:              1 set

8) Product Rack (un-powered):         1 set (two pieces, total length is 3 meters)

- TECHNICAL SPECIFICATION:

(1) Manual decoiler

1) Un-power; manual decoiler;  max. Capacity: 3000kg

2) Suit for coil inner-diameter: 508mm, suit for coil max outer diameter: 1000mm

3) Manual power expands the coil inner surface.

The decoiler out form reference:

(2) Leveling Equipment

Make the steel strip go into the cutting equipment flatly and straightly, which ensures the controller measures the size of steel strip precisely and the feature of flat and straight purline production.

(3) Punching system

1) Adopt welded steel frame, it has great rigidity.

2) Round holes as per profile. the horizontal punch distance of the hole can be adjusted manually; vertical position is to be adjusted by inputting parameters into the PLC.

3) Punching die material: Cr12 mould steel.

(4) Roll-Forming M/C

1) The main frame of machine is welded separately and the outside wall is connected by screw

after being rotoblasted on the surface.

2) Roller Material is Cr12 mould steel being quenched treatment, with digital-controlled

procession.

3) Shafts of rollers are tooled by grinding machine for two times to ensure the precision of final

product.

4) The rollers are plated with hard chrome with thickness of 0.05mm on the surface after being

machined by the exact machine tool. So that ensure long life of forming rollers.

6) Shaft diameter is 82mm.

7) Chain and gear move the line, motor drives. All working actions are controlled by PLC electric cabinet automatically.

8) Suitable power voltage: 380V/50HZ/3Phase (can de designed according to buyer’s

requirement)

9) Line working speed (Forming speed)：about 8-10m/min (without cut time)

10) Main machine motor power: 15KW(Depend on final design)

Roll forming system

Tolled forming rollers

(5) Hydraulic Cutting

1) Adopts post cutting, Stop to cut;

2) The cutting blade material is Cr12 with quenched treatment.

3) Adopts welded frame for good rigidity.

4) Cutting frame has been heat treatment to avoid final product deformation. cutting length

tolerance ±2mm.

5) The power of cutting is provided by hydraulic station.

6) The final product can be cut as per set length in PLC controller, and the length is automatically

measured by encoder. When final product reaches the set length, machine will stop to cut the

product automatically. Finish this action, machine will run again continuously.

(6) Hydraulic station

1) It supplies the power for the hydraulic cutter.

2) All hydraulic accessories are all use Chinese famous brand products.

3) Hydraulic motor power: 5.5KW

(7) PLC Control System

1) This system uses Mitsubishi PLC to control the all working actions. Production quantity and

each piece length will be automatically measured. It is convenient to control the roll forming

machine.

2) Mitsubishi converter adjusts speed technology, realize the automatic production.

3) Touch screen is input and cancelled the working data.

4) Friendly man-machine interface system can be set batches to the workpiece, length, quantity,

etc.

5) Encoder count, having function of count and measuring length.

6) Suitable power voltage: 380V/50HZ/3Phase (can de designed according to buyer’s requirement)

System outer form reference:

(8) Product Rack (un-powered)

1) They are used to put the final product when product coming out from cutting device.

2) Two pieces, each piece length is 1.5m, total length is 3 meters.

3) Collect the final product and final products is convenient to be stacked by workers.

Outer former reference:

- Line working processing display

Decoiling the sheet → Leveling sheet→ Punching→ Roll forming→ Measure length and cutting→ the Purline to the supporter

- Reference view of machine:

- Reference Layout drawing of machine