Quotation

We supply The DYFD-100-1 High Speed twist-rope & Flat-belt handle machine, the newest detail information as follow:

Performance And Characteristics:

This is a high-speed machine for producing paper handles, it pastes twist paper ropes and paper together for handles, then cut off then in separate automatically. Besides, it has the functions of handles counting, handles putting in order and handles colling. It is and ideal supporting machine of paper Handbag Making Machine.

Main Technical Parameter

| Maximum Speed (bag/min.) | 100-300 |
| --- | --- |
| Total Power (kw) | 6 |
| Machine Weight (Ton) | 3.5 |
| Machine Dimension (L*W*H) | 6000*1800*1800mm |
| Twist rope handle |
| Handle length | 105-155mm |
| Handle width | 95mm |
| Paper board width | 35-55mm |
| Paper board length | 190mm |
| Paper board weight | 100-120g/㎡ |
| Rope diameter | 3-5mm |
| Flat belt handle |
| Handle length | 105-155mm |
| Handle width | 95mm |
| Paper board width | 35-55mm |
| Paper board length | 190mm |
| Paper board weight | 100-120g/㎡ |
| Rope width | 10-12mm |

DYFD-100-2 Right-angel Flat belt Handle Machine

Performance And Characteristics:

This machine is the latest new supporting machine for Paper Handbag Making Machine developed by us. It is the machine that can make the cut four roll paper into the right angle flat-belt paper handle after the complex craft.

Main Technical Parameter

| Maximum Speed (bag/min.) | 100-150 |
| --- | --- |
| Total Power (kw) | 8 |
| Machine Weight (Ton) | 4 |
| Machine Dimension (L*W*H) | 5000*1800*1800mm |
| Right Angle Flat-belt handle |
| Handle length | 105mm |
| Handle width | 102mm |
| Paper board width | 35-50mm |
| Paper board length | 204mm |
| Paper board weight | 100-120g/㎡ |
| Rope width | 10-15mm |