Fujian Aivyter Compressor Co., Ltd

Office Add: # 505 No.3 Building, XiaoqiaoXinyuan, No.587 Liuyi North Road, Fuzhou, China

Contact Person: Vivien           Email Add.: vivien@aivyter.com

Skype: Vivien.yao115           MSN: Viviem115@hotmail.com

Tel: 86-591-83753886           Fax: 86-591-83790287

Phone: 86-18259009386           Website: en.aivyter.com

Quotation

- Main Performance Parameters & Price of SG08~SG75 (10HP-100HP)

Belt Driven Screw Air Compressors

| Model | SG08 | SG11 | SG15 | SG18 | SG22 |
| --- | --- | --- | --- | --- | --- |
| Motor power | Kw | 7.5 (10hp) | 11 (15hp) | 15 (20hp) | 18.5 (25hp) | 22 (30hp) |
| Capacity/ Pressure | (m3/min /bar) | 1.20/7 | 1.65/7 | 2.25/7 | 3.22/7 | 3.60/7 |
|  |  | 1.10/8 | 1.53/8 | 2.03/8 | 3.00/8 | 3.56/8 |
|  |  | 0.95/10 | 1.32/10 | 1.82/10 | 2.52/10 | 3.07/10 |
|  |  | 0.80/12 | 1.10/12 | 1.55/12 | 2.30/12 | 2.84/12 |
| Cooling mode | Air cooled | Air cooled | Air cooled | Air cooled | Air cooled |
| Driven mode | Belt driven | Belt driven | Belt driven | Belt driven | Belt driven |
| Starting mode | Direct | Y-△ | Y-△ | Y-△ | Y-△ |
| Dimension mm | L | 900 | 1000 | 1000 | 1100 | 1100 |
|  | W | 700 | 900 | 900 | 1000 | 1000 |
|  | H | 900 | 1200 | 1200 | 1350 | 1350 |
| Gross weight | Kg | 300 | 450 | 500 | 550 | 600 |
| Noise level | dB(A) | 62±2 | 63±2 | 63±2 | 63±2 | 65±2 |
| Outlet diameter | G3/4″ | G3/4″ | G3/4″ | G1 1/4″ | G1 1/4″ |
| FOB Price USD |  |  |  |  |  |

| Model | SG30 | SG37 | SG45 | SG55 | SG75 |
| --- | --- | --- | --- | --- | --- |
| Motor power | Kw | 30 (40hp) | 37 (50hp) | 45 (60hp) | 55 (75hp) | 75 (100hp) |
| Capacity/ Pressure | (m3/min /bar) | 5.20/7 | 6.58/7 | 7.36/7 | 10.8/7 | 13.5/7 |
|  |  | 5.06/8 | 6.26/8 | 7.10/8 | 10.1/8 | 12.7/8 |
|  |  | 4.53/10 | 5.80/10 | 6.47/10 | 8.50/10 | 11.3/10 |
|  |  | 3.90/12 | 5.06/12 | 5.80/12 | 7.69/12 | 10.0/12 |
| Cooling mode | Air cooled | Air cooled | Air cooled | Air cooled | Air cooled |
| Driven mode | Belt driven | Belt driven | Belt driven | Belt driven | Belt driven |
| Starting mode | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ |
| Dimension mm | L | 1100 | 1300 | 1300 | 1800 | 1800 |
|  | W | 1000 | 1100 | 1100 | 1300 | 1300 |
|  | H | 1350 | 1500 | 1500 | 1700 | 1700 |
| Gross weight | Kg | 800 | 1100 | 1250 | 1950 | 2000 |
| Noise level | dB(A) | 65±2 | 65±2 | 68±2 | 68±2 | 72±2 |
| Outlet diameter | G1 1/4″ | G1 1/2″ | G1 1/2″ | G2″ | G2″ |
| FOB Price USD |  |  |  |  |  |

- Main Performance Parameters & Price of SGD22~SGD250 (30HP-350HP)

Direct Driven Screw Air Compressors

| Model | SGD22 | SGD30 | SGD37 | SGD45 | SGD55 | SGD75 | SGD90 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Motor power | Kw | 22 (30hp) | 30 (40hp) | 37 (50hp) | 45 (60hp) | 55 (75hp) | 75 (100hp) | 90 (120hp) |
| Capacity/ Pressure | (m3/min /bar) | 3.60/7 | 5.20/7 | 6.58/7 | 7.36/7 | 10.8/7 | 13.5/7 | 16.2/7 |
|  |  | 3.56/8 | 5.06/8 | 6.26/8 | 7.10/8 | 10.10/8 | 12.7/8 | 15.2/8 |
|  |  |  | 4.53/10 |  | 6.47/10 |  | 11.3/10 | 14.3/10 |
|  |  |  | 3.90/12 |  | 5.80/12 | 7.69/12 | 10.0/12 |  |
| Cooling mode | Air cooled | Air cooled | Air cooled | Air cooled | Air cooled | Air cooled | Air cooled |
| Driven mode | Direct driven | Direct driven | Direct driven | Direct driven | Direct driven | Direct driven | Direct driven |
| Starting mode | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ |
| Dimension mm | L | 1300 | 1300 | 1500 | 1500 | 1900 | 1900 | 1900 |
|  | W | 800 | 800 | 1000 | 1000 | 1200 | 1200 | 1200 |
|  | H | 1150 | 1150 | 1350 | 1350 | 1500 | 1500 | 1500 |
| Gross weight | Kg | 580 | 780 | 820 | 900 | 1800 | 2000 | 2200 |
| Noise level | dB(A) | 63±2 | 63±2 | 63±2 | 65±2 | 65±2 | 68±2 | 68±2 |
| Outlet diameter | G11/4″ | G11/4″ | G11/2″ | G11/2″ | G2″ | G2″ | G2″ |
| FOB Price USD | 2465 |  | 3598 |  | 6800 | 7717 | 9567 |

| Model | SGD110 | SGD132 | SGD160 | SGD185 | SGD220 | SGD250 |
| --- | --- | --- | --- | --- | --- | --- |
| Motor power | Kw | 110 (150hp) | 132 (175hp) | 160 (200hp) | 185 (250hp) | 220 (300hp) | 250 (350hp) |
| Capacity/ Pressure | (m3/min /bar) | 21.6/7 | 25.2/7 | 28.7/7 | 32.5/7 | 36.8/7 | 42.7/7 |
|  |  | 20.1/8 | 24.0/8 | 27.6/8 | 30.8/8 | 34.7/8 | 40.8/8 |
|  |  | 17.5/10 | 21.0/10 | 25.3/10 | 28.2/10 | 30.8/10 |  |
|  |  | 16.0/12 |  | 22.4/12 | 25.1/12 | 28.9/12 |  |
| Cooling mode | Air/water cooled | Air/water cooled | Air/water cooled | Air/water cooled | Air/water cooled | Air/water cooled |
| Driven mode | Direct driven | Direct driven | Direct driven | Direct driven | Direct driven | Direct driven |
| Starting mode | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ | Y-△ |
| Dimension mm | L | 2200 | 2200 | 2400 | 2400 | 3100 | 3100 |
|  | W | 1600 | 1600 | 1650 | 1650 | 2150 | 2150 |
|  | H | 1800 | 1800 | 1900 | 1900 | 2350 | 2350 |
| Gross weight | Kg | 3000 | 3600 | 3880 | 4050 | 4700 | 5100 |
| Noise level | dB(A) | 68±2 | 68±2 | 72±2 | 72±2 | 76±2 | 76±2 |
| Outlet diameter | DN65 | DN65 | DN80 | DN80 | DN80 | DN80 |
| FOB Price USD | 13335 | 13884 | 16150 | 17617 | 26500 | 28334 |

- Business Terms

1) Payment terms: T/T 30% down payment after sign the contract, T/T 70% before shipment.

2) Delivery time: in 15-20 days after received 30% down payment.

3) The guarantee period is one year for air compressors and two years for air end. Offering maintain suggestions.

4) Packing: standard export packing.

5) The above offer is valid for 3 months.