QUOTATION

| No. | Commodity | Quantity | Unit price | Amount |
| --- | --- | --- | --- | --- |
| 1 | RY-330 flexo label printing machine (include5printing units 5 Taiwan UV dryer 1 BST camera 1 lamination system 1 turn bar 1 web-guide 1 waste collection 3 die cutting station 2tesion controller 15 printing cylinder 5 Anliox cylinder) | 1 unit | USD59000.00 | USD59000.00 |
| Options |
| 1.1 | Cold stamping | 1 unit | USD2000.00 | USD2000.00 |
| Total value: |  |

1)RY330 flexo printing machine with 5 colors

Printing speed:around 60m/min

Max Printing color: 6

Max web width: 330mm

Max print width: 320mm

Max unwind diameter: 650mm

Max rewind diameter:600mm

Print length: 175-380mm

Main power: 380V/AC(3 PHASE)50HZ

The thickness of substrate:0.1~0.3mm

:Package size: 12CBM

Gross weight: 2500kgs

Net weight: 2000kgs

Tention control (unwind): Japan

Tention control (rewind): China

Main motor: China

Transducer: Taiwan

Printing cylinder: 3set*5=15pcs (57teeth to 120teeth)

Anliox roller: 5pcs (300lines to 1000lines)

The machine with web guide, turn bar, waster wrapper.

1) Printing roller: 3sets, the size is determined by the user from 57teeth to 120teeth

2)anilox cylinders:  1set, the lines can be chosen from 200 to 1000 by the user.

3) Mounting machine: 1 set

4) turn bar: 1set

5) unwind tension controller: 1piece Mitsubishi of Japan

6) transducer: 1pc Taiwan

7) rewind tension controller: 1piece made in China

8) magnetic power brake:3pcs  China

9) electromagnetism valve: 2pcs Japan

10) inverter: Taiwan

11) stop automatic when paper lack

12) machine stop automatic when the paper broken

13) Contactor: Schneider France

14) time replay: 1pc Taiwan

15) solid reply: 2pcs Japan

16) Temperature Controller: China

17) All air Switches: Schneider France

18) Other low-pressure wiring Schneider? France/ China

All the rollers are deal with high temperature.

Characteristics:

1)  The main motor adopts imported inverter to govern a stepples speed adjustment.

2) The printing units are all equipped with a group of infrared dryers respectively.

3) Each IR dryer device of printing unit

4) Feeding and rewinding are controlled through magnetic particle brake and clutch

(Japanese Mitsubishi auto tension controller).

5) Un winder and re winder adopt air core holder.

6)one unit rotary station

7) Adopt ceramic anliox roller which offers  durability, wear resistance and corrosion resistance, also is more efficient on production by reducing the times of

changing rollers.

8) The printing unit can register in 360 degrees. Each printing unit can be

independently geared and loosen to have rest of units continue to printing.

9) The inking roller will be automatically off impression when press stop and rotate

at lower speed in order to keep the ink from being drying.

10) Paper unwind, printing, laminating, rotary diecutting, waste removal

and rewinding can be processed in one pass. It has characterized by wide

application, fast printing speed and high economic efficiency ink will not

contaminate environment. So it is an idea printing machine for the business form,

Tag and high end pressure sensitive label.

Sample:

2) Other information:

A. Packing: Sea worthy wooden case

B.Quality Guarantee: within one-year guarantee from B/L date. If the machine need repair   within this period, the seller shall dispatch technician to buyer’s side in time. But the buyer shall bear all the expense during the repair period.

C.Term of trade: FOB Wenzhou, shall be subject to the International Rules for the Interpretation of Trade Terms (INCOTERMS 2000) Provided by International Chamber of Commerce (ICC)

D.Payment: 30% T/T payment for deposit, 70% T/T payment before shipment.

E.Delivery time:40 days after receiving the 30% T/T payment.

F.Insurance: to by covered by buyer

G.Expense for installment and test machine: The seller will dispatch the engineer to buyer side in time when the machines arrive at buyer’s place. The buyer pays all the expenses including the go and come back air-ticket, feeding and accommodation during the testing machine period.

H.Time of install and testing machine at buyer side: 5 days

This quotation is valid for 30days.

If you want to know more information, please feel free let us know.

Best Regards

Jared Lin,