Wuxi Zhenda Automation Equipment Co., ltd

| Type | ZLP630(6m) |
| --- | --- |
| Rated load | kg | 630（ including the weight of personnel ） |
| Lifting speed | m/min | 9.3±0.5 |
| Dimension of platform (length×width×height) | mm | (2000x3)×690×550 |
| Suspension Mechanism | protrusion of front Beam | mm | 1300 |
|  | Height of Front Beam | mm | 1300~1800 （ adjustable distance 100） |
| Hoist | Type |  | LTD6.3 |
|  | Quantity | piece | 2 |
|  | Motor | Type |  | YEJ90L-4 |
|  |  | Power | kW | 1.5 |
|  |  | Voltage | V | 220 |
|  |  | Rotation Speed | r/min | 1400 |
|  |  | Brake Torque | N-m | 15 |
| Safety Lock | Type |  | LSG20 |
|  | Quantity | piece | 2 |
|  | Allowable Impulsive Force | KN | 20 |
| Weight | Suspension Platform | kg | 181 |
|  | Hoist | kg | 50×2 |
|  | Safety Lock | kg | 5.5×2 |
|  | Suspension Mechanism | kg | 312（ no-including Counter weight ） |
|  | Electric Control Box | kg | 16 |
|  | The Whole Machine | kg | 619 |
|  | Counterweight | kg | 900（25×36pcs） |
| Wire Rope | Type |  | 4×25Fi+PP-Φ8.3 Break Strength ≥51800N |
| Power Cable | Type |  | 3×2.5+2×1.5YC-5 |

Major technical data of ZLP630(6 m) aluminum type