SJ-65D/FM1200 Film Blowing Machine

1.挤出机

1.1螺杆:螺杆直径Φ65

长径比:28:1;材料:38CrMoALA

1.2螺杆转速：10-100r/min

1.3机筒：机筒加热:铸铝加热圈

机筒冷却：第三区风冷

冷却风机：350W

1.4减速器： 1:5齿轮箱

1.5挤出主电机：22KW科沃变频器

1.6温度传感器：3个

2.换网器

2.1手动拆卸换网装置

2.2换网器加热：不锈钢加热圈

2.3温度传感器：1个

3.模头

3.1基本结构型式：单层螺旋模头结构

3.2模头材料：40Cr模具钢

3.3模头规格：Φ220-120㎜

3.4模头加热:不锈钢加热圈

3.5温度传感器：1个

4.风环

4.1结构型式:单风口风环

4.2材料:铸铝

4.3风机功率:1.5 KW

5.稳泡器

5.1结构型式:摆杆式

6人字板

6.1结构型式:木条式

6.2调节方式:手动

7.插边器

7.1结构型式:绒布式

7.2调节方式:手动

8.牵引

8.1结构型式: 固定架

8.2牵引电机: 科沃变频1.5KW

8.3牵引辊夹紧方式手动夹紧装置

8.4薄膜最大折径:1200㎜

8.5胶辊长度:1300㎜

9.收卷机

9.1双工位背靠背摩擦收卷机

9.2力矩调速器  3只

10.牵引机架

10.1方型一体化牵引机架,配备斜梯

二色1200mm柔性凸版印刷机

一：主要参数 ：

1、机器型号：1200mm

2、印刷材料 ：无纺布、卷筒纸、淋膜纸、 薄膜、铝箔、薄皮等各种软包装卷状材料。

3、最大印刷宽度 ：1100mm

4、最大印刷长度 ：100-1000mm

5、印刷速度 ：10-50m/min

6、版材厚度（包括双面胶）：2.38mm

7、机器尺寸：3500*2400*1800mm

8、整机重量：2000kg

二：放料部分：

1、辊长：1250mm

2、有效印刷辊长：1100mm

3、辊芯直径 76mm

4、放料最大直径： 1000mm

5、放料方式：摩擦式

三：牵引部分：

1、牵引组成： 皮辊 镀铬辊

2、组数 ：2组

四：印刷部分：

1、印刷组成： 镀铬辊、版辊、网纹辊、胶辊

2、版辊周长 ：100-350mm

3、印刷版材  ：树脂版材或橡皮版材

4、传动方式 ：齿轮带动

5、印刷套色： 360度旋转

6、调节方式： 手动

7、起落版调节： 手动

五：加热烘干部分

1、加热烘干方式：先吹风机再加热

2、加热区：  2色：2根

3、加热功率： 3kw

4、辅助烘干长度：1米

5、风机：2个

6、风机功率：1200mm ：0.75kw  0.75 kw

六：电机部分：

主电机： 3kw

运墨电机： 0.55kw

3、主机采用变频器控制调速

七：收卷部分

1、辊长：1250mm

2、有效辊长：1250mm

3、辊芯直径：76mm

4、放料最大直径 ：1000mm

5、收卷方式 ：摩擦式

八：主要详细配置清单

主电机（变频电机）：  1件 ：3KW（上海速川）

运墨电机：   0.35kw（上海速川）

主机变频器：1套（惠丰）

风机：2件   2*0.75KW（上海丰扬）

铝导辊：（表面氧化，动静平衡处理）

网纹辊：一色一条（温州）

胶辊：一色一条：（自产）

磁粉：一套（上海海泰磁粉有限公司）

张力控制器：（上海张力自动化设备有限公司）

低压电器：（中国正泰集团）

光电纠编：一套（自产）

气涨轴：2条（瑞安强光机械厂）

开关：（法国施耐德）

电器控制箱：1套（自产）

主机架1组：（自产）

整机铸件：（自产）

气动元件：（上海创峰气动）

1300电脑控制自动分切机

| 主电动机 | 4KW（上海产） |
| --- | --- |
| 主机变频 | 4KW(台州产) |
| 光电眼 | 纠偏用（龙游） |
| 磁粉 | 5kg（胜设产） |
| 同步电机 | 110W（无锡产） |
| 滚珠丝杆 | 纠偏用（无锡产） |
| 纠偏控制线路板 | 纠偏用（三菱技术） |
| 张力控制线路板 | 控制张力用（三菱技术） |
| 张力电流表 | 调节张力电流（三菱技术） |
| 记米器 | 记米用（三菱技术） |
| 线速度测量计 | 测线速度用（三菱技术） |
| 主电机电位器 | 调主电机速度用（三菱技术） |
| 离心式通风机 | 550W |
| 平刀15副 | 进口 |
| 压棍四条 | 收料使用 |
| 气胀轴3条 | 收料使用 |
| 槽棍一条 | 平刀使用 |

TRB-1300 Auto threading-rolling bag-making machine

Characteristics:

This machine is researched and manufactured by our company on the basis of  integration of advanced foreign technology. It adopts the materials like LDPF,

LHPF and cylinder film to manufacture threading garbage bags or folded-rolled bags. The machine adopts computer control, servo, a step motor to fix the

length, photoelectric tracking, auto counting, alarming up to the set number, auto rectifying and auto etc. It is an idea equipment to manufacture threading

garbage bags.

| Model | TRB-1300 |
| --- | --- |
| Max. Bag-making width | 1300mm |
| Max. Bag-making length | 999mm |
| Bag-making thickness | 0.015-0.05mm |
| Bag-making speed | 20-50pcs/min |
| Varieties of bags | (printing bags, Uncolored bags) |
| Total power | 10kw |
| Weight of machine | 2600kg |
| Overall dimensions | 9800×2400×2000mm |

| Main Components |
| --- |
|  | Name | Origin |
| 1 | Liquid Crystal Display | From Wuxi City 无锡 |
| 2 | Electric switch | Schneider 施耐德 |
| 3 | Stepping motor | Made in China 中国制造 |
| 4 | Main Motor | From Shanghai 上海 |
| 5 | Electrical switches | Schneider 施耐德 |
| 6 | air cylinder | Yadeke from TaiWan 亚德客 |
| 7 | DC delivery motor | 600w from Wuhu 芜湖 |
| 8 | DC feeding motor | 600w from Wuhu 芜湖 |
| 9 | Stringing delivery motor | 300w from Wuhu 芜湖 |
| 10 | Inverter | Huifeng from yantai 惠丰 |
| 11 | Solid-state Relay | From Magnate |
| 12 | Electromagnetic watts | Yadeke from TaiWan 亚德客 |
| 13 | Main Photoeye | Made from China 中国制造 |
| 14 | Computer rectifying edge | Made in China中国制造 |
| 15 | Temperature controller | Made in China中国制造 |
| 16 | Synchronous motor | Made in China 中国制造 |
| 17 | Feeding width of material | 900mm |
| 18 | Dia. of feeding material | 600mm |
| 19 | Airshaft | Made in china 中国制造 |
| 20 | Magnetic powder | Made in China 中国制造 |
| 21 | Rubber Roller | Made of Wear-resisting Rubber Materials |
| 22 | silica gel Roller | Made of thermostability material 稳定材料 |
| 23 | Punching part | Changrong from shenzhen 长荣 |
| 24 | Round hole | 30mm |
| 25 | Side sealing heat knife | 2 pieces, Copper |
| 26 | Main Point broken knife | Our factory 本厂制造 |
| 27 | Main Heat blade | Our factory 本厂制造 |
| 28 | Main Point broken Blade | Ma’an shan Factory马鞍 |
| 29 | Round hole | 60mm 2 pieces |
| 30 | Crevasse | Our factory 本厂 |
| 31 | Plastic string width | 15-35mm |
| 32 | Running roller | Aluminum |