无锡贝瑞斯机械设备有限公司

WUXI BALANCE MACHINERY EQUIPMENT CO., LTD

Add: 1112, No. 158, Wangzhuang Road, Wuxi City, Jiangsu Province, China

Tel: 0086-510-83115339    Fax: 0086-510-83113616    Mobile: 0086-158-616-98920

Skype: platform_balance       MSN: platform_balance@hotmail.com

Email: angela@cnplatform.com            Web: www.cnplatform.com

Contact: Angela Wang

QUOTATION

To: Mr. Hamid Ra                                        Quote No.: 13BRS011204

(1kg = 2.2lbs, 1inch = 25.4mm, 1feet = 0.3048m)

| Mobile Scissor Work Platform – Manual Push |
| --- |
| Model | Configuration | Quantity |
| SJY0.5-11 | Rated Capacity (kg) | 500 | 1 Set |
|  | Min. Height (mm) | 1680 |  |
|  | Platform Height (mm) | 11000 |  |
|  | Working Height (mm) | 12700 |  |
|  | Platform Size (mm) | 2000*1200 |  |
|  | Motor Power (kw) | 2.2 kw |  |
|  | Self weight (kg) | 1500 |  |
|  | Voltage | 220V/3Ph/60Hz |  |
|  | Outside dimension (mm) | 2000*1300*1680 |  |
|  | Package dimension (mm) | 2150*1450*1780 |  |
| FOB SHANGHAI PORT, CHINA ------ US$ 5,000/ SET (Delivery by LCL with other client’s products) (Packed by pallet) |

Above includes the following configuration:

| No. | Name | Configuration |
| --- | --- | --- |
| 1 | Material of platform | 4mm antiskidding diamond plate, 1000mm guardrail |
| 2 | Main beam of Scissor materials | Q345B high strength manganese steel 120*40*4 rectangular tube |
| 3 | Cylinder | Diameter: 80mm (3 Pcs) |
| 4 | Cylinder facing bar | Q345B high strength manganese steel |
| 5 | high-pressure oil tube | High pressure Double-layer steel wire mesh structure 602-0802-48.0MPa |
| 6 | Hydraulic medium | 32# wear-proof hydraulic medium |
| 7 | appliance | Relay, Contactor, Push Button, etc |
| 8 | sealing element | UHP, Y type sealing element, Rubber O -rings |
| 9 | Gear wheel pump | 1 Pcs |
| 10 | Supporting valve | 1 Pcs |
| 11 | Motor power | 2.2 kw |
| 12 | Movable tire | 4 pcs 400-8 air-filled tyre |
| 13 | Paint | Vehicle specific paint |
| 14 | Connection of Base plate and Scissor | Equip 4mm flat slab Scissor coupling mechanism adopt pouring steel castings |
| 15 | Voltage | 220V/3 PHASES /60HZ |
| Note: 1. Center pin and edge pin: heat treatment 2. Connecting material: 506 welding, gas shielded arc welding 3. Overall hook: CNC wire cutting 4. It equips with emergency descending device when power-off, over-load protect device, explosion prevention device |

Summary:

- Terms of validity: 1 month

- Payment: USD 100% paid in advance by T/T.

3.  Time of Delivery: 20 working days after receipt of the payment.

4.  Warranty: 1 year