QUOTATION

We supply SLW-1200 Double Layers Stretch Film Production Line, the newest information and quotations as follow:

Ⅰ.Feature:

1. It profits advanced technology from aboard and manufacture by absorption, improvement, innovation.

2. It is entire frequency conversion control, movement stable, highly effective and the low energy consumption.

3. The product adopts the craft of one time forming.

4. It can produce two-side sticks for stretching film.

Ⅱ. Unit introduction

1. This series unit is mainly used in producing the polyethylene plastic film for unidirectional stretch (stretching film, twines membrane) as well as fresh film.

2. Therefore it applies in building material, hardware fitting packing widely. The screw of unit adopts 38CRNOALA alloy steel. It manufactured by nitric and precise processing so that it is highly hardness and durable long time.

3. Temperature controls adopts advanced automatic control system and the T mold adopts the multi- spots adjustment. They could cause the film thickness to be evener.

4. The cooling system adopts the circulating water cool and it cooling effect is good.

5. The rollout installment adopts the friction type of rollout and has the cutting edge installment and side material rollout element by round-trip. This causes the film which rollout to be neater.

Ⅲ. Main Technical Parameter

| Model: | SLW-1200 double layers | SLW-1200 |
| --- | --- | --- |
| Screw Diameter | 60mm×2 | 65mm |
| L/D ratio | 28:1 | 28:1 |
| Screw Barrel Material | 38CRMOLA | 38CRMOLA |
| Die width | 1450mm | 1450mm |
| Film Width | 500-1200mm | 500-1200mm |
| Thickness | 0.008-0.05mm | 0.008-0.05mm |
| Rollout Diameter | 300mm | 300mm |
| Output | 70-90kg/h | 65kg/h |
| Main Motor Power | 15kw×2 | 15kw |
| Heating Power | 65kw | 65kw |
| Overall dimension: | 6000×3000×2600mm | 6000×2200×2500mm |
| Total Weight | 5000kg | 4500kg |

| Standard configuration |
| --- |
| Item | Description | quantity |
| 1 | Automatic Winding changer | 1pcs |
| 2 | Automatic Air shaft | 2pcs |
| 3 | Automatic Trimming device | 1pcs |
| 4 | Automatic Temperature Control | 12unit |
| 4 | Step less Inverter | 1set |
| 5 | Step Motor | 1set |
| 6 | AC Motor | 1set |
| 7 | Gear box | 1set |
| 8 | Panel box | 1set |
| 9 | Switch (ZHENGTAI) | Several pcs |
| 10 | Electrical component (ZHENGTAI) | Several pcs |
| 11 | Hopper | 2pcs |
| 12 | Cooling roll (diameter: 270mm) | 1pcs |
| 13 | Air compressor | 1pcs |

| Spare Accessories |
| --- |
| Item | Description | Quantity |
| 1 | Tools | 1pcs |
| 2 | Instructions | 1pcs |
| 3 | Schematic | 1pcs |
| 4 | Current meter | 1pcs |
| 5 | Voltage meter | 1pcs |
| 6 | Thermocouple | 1pcs |
| 7 | Relay | 1pcs |
| 8 | Out color | Dark blue |

Ⅳ. Quotation (F.O.B Price to Ningbo port)

| Model | Price |
| --- | --- |
| SLW-1200 single layer | 24000USD |
| SLW-1200 double layers | 37000USD |

Our price valid period last for 2 months.

Optional Device with Extra

Item                Unit Price       Discount price

1).Auto loader             750USD/Piece       1400USD/Two Pieces

2) Dry Hopper             450USD/Piece       800USD/Two Pieces

3) Auto Screen Changer     850USD/Piece       1500USD/Two Pieces

4) Glue Pump             750USD/Piece       1400USD/Two Pieces

5) Mixer					2400USD/SET		  2200USD

6) Air Compressor	       200USD	         150USD

7) Chiller                 2000USD           2000 USD

Ⅴ.Delivery

Within 30 days shipment the machine， we manufacture the machine after we receipt 30% deposit.

Ⅵ.Guarantee

- One year guarantee the quality of machine. But the buyer need pay the cost of maintenance if it is break down due to incorrect operation.

- Spare parts attached for free, problem parts can be changed for free in 1 year, but the express fee should be paid by users, others(if needed) suggest to be bought at the first time to save the cost of transportation.

Ⅶ. Technical services

- We will teach your staff to learn all the operation instruction in our factory if needed, this operation is easy to learn and only 1 person is enough to control !

- If need our engineer go to your country or teach and install ,the flight fee, the living fee, engineer salary (60 USD/per day) should be in charge by buyer

- We would present buyer the specification and Video or CD along with the machine when shipment.

Ⅷ. Package

In wooden box, or stretch film package or in bulk just according to the situation of shipment or clients, wooden box need pay extra package charge.

Extra Equipment Details

1. DYFS-60 stretching film crusher & mixer

Application:

The machine is characterized by sound reliability, easy maintenance and stability in design. It is specially applied to recycling the hydrostatic film materials and other materials, such as CPE，PE，PO，PP，PET，PA and etc, which will bring you sound economic result. It is suitable for crushing the stretching film with some glue, it is of excellent operation system and high output capacity.

Characteristics:

It only recycles directly the film materials without changing the chemical contents or compositions so the pellet can be recycled to utilize. Its master motor adopts import name converter to govern, which is characterized by saving power, good for environmental protection ,simple construction, ease of operation(one person operation ) and high automation.

Main Technical Data:

| Main Motor Power | 3kw |
| --- | --- |
| Machine Weight | 300kg |
| Overall Dimensions | 700*700*1600mm |

2. Industrial Air Cooled Chiller

A. Technical Parameters

| Model Item | AC-3 |
| --- | --- |
| nominal cooling capacity | kcal/h | 6803 |
|  | kw | 7.91 |
| input power | kw | 3.33 |
| power supply | 3PH~380V/50HZ |
| refrigerant | type | R22 |
|  | type of control | capillary |
| compressor | type | hermetic scroll(piston) |
|  | power(kw) | 2.8 |
| condenser | type | finned copper tube + low noise outer rotor fan |
|  | cooling air flow (m3/h) | 3000 |
| evaporator | type | tank with coil(shell and tube) |
|  | chilled fluid flow (m3/h) | 1.36 |
|  | volume (L) | 50 |
|  | inlet and outlet pipe diameter (inch) | 1 |
| water pump | power (kw) | 0.37 |
|  | lift (m) | 20 |
| safety protection | compressor over temperature, over current, high and low pressure, over temperature,flow switch, phase sequence, phase-missing, exhaust overheating, antifreezing |
| weight | kg | 135 |
| dimension | mm | 930*520*975 |

- Note: 1. Nominal cooling capacity is according to:

- Inlet chilled fluid temperature: 12℃

- Outlet chilled fluid temperature: 7℃

- Inlet cooling air temperature: 30℃

- Outlet cooling air temperature: 38℃

- 2. Working range:

- The temperature range of chilled fluid is from 5℃ to 35℃;

- Temperature difference between inlet and outlet chilled fluid is from 3℃ to 8℃.

- It is better to use the chiller while the ambient temperature at or below 35℃.

- We reserve the right to modify the above dimensions or parameters without further notice.

B. Main parts of 3-5 HP Air cooled chiller

| Main parts | Brand | Origin |
| --- | --- | --- |
| Compressor | Hitachi | Japan |
| Electrical components | Schneider | France |
| Water pump | Pentax | Italy |
| Evaporator | ANGES | Hong Kong |
| Condenser | ANGES | Hong Kong |
| Pressure Controller | JUNLE | TAIWAN |
| Oil type pressure gauge （High pressure） | HONGSEN | CHINA(Taiwanese capital) |
| Oil type pressure gauge (Low pressure) | HONGSEN | CHINA(Taiwanese capital) |
| Thermostat | ANGES | Hong Kong |
| Expansion Valve | ALCO | America |
| Filter Dryer | ALCO | America |
| Cooling Fan(outer-rotor blower) | MAER | TAIWAN |

3. Air compressor

Application: it is used for stock and compress the air, adjust air load, delay to use the air.

Detail specification:

| Item | Air compressor |
| --- | --- |
| Pressure | 0.8Mpa |
| Weight | 80kg |
| Dimension | 900×450×790mm |
| Power | 1.5kw |

4. Auto feeder

Feature:

1. Small dimension, light weight, can be install on the dryer or other raw material holder.

2. It adopt microcomputer control, unload or shortage material automatic alarming.

3. High speed motor, convenient operate, lower noise, long use time.

Main Specification:

| Item | Auto feeder |
| --- | --- |
| Motor | 1kw |
| Speed | 200kg/h |
| Capacity | 6L |
| Lift | 5-7m |
| Weight | 13kg |

5. Glue Pump

Application: This glue pump used for put glue into the raw material and produce the stretch film.

Main specification

| Item | Glue pump |
| --- | --- |
| Volume | 5kg |
| Material | Stainless steel |
| Power | 0.5kw |
| Weight | 50kg |

Gear Box                                     Hopper

Packing: with stretch film and bubble film.

It also can be packing with wooden box (you need to pay the extra fee)