Polishing machine for spoon

Summary

These machines are designed for polishing curved surfaces of stainless steel forks and spoons. The polishing process is competed automatically after the working piece is mounted. The pneumatic driver has a simple structure and low costs. A high performance to costs ratio is realized because of its reliability. Comparing to a machine with mechanical driver, these machines have the advantage of adjustable work speed and travel distance, more stable operation, longer service life and lower maintenance costs, ect.

Main technical data

Hydraulic automatic polisher  (YP-01  YP-04)

| Type | YP-01 | YP-04 | 单位 Unit |
| --- | --- | --- | --- |
| Polishing Wheel | Speel | Upper shaft | 2000 | 2800 | r/min |
|  |  | Lower shaft | 2000 | 2000 | r/min |
|  | Length | 620 | 620 | mm |
| Worktable | Maximum horizontal traveling distance | 50 | 50 | mm |
|  | Maximum vertical travel distance | 350 | Manual | mm |
| Motor | Upper shaft | 5.5 | 5.5 | KW |
|  | Lower shaft | 5.5 | 5.5 | KW |
| Hydraulic system working pressure | 1.5-2 | 1.5-2 | Mpa |
| Dimensions (L*W*H) | 2000*1400*1700 | 2000*1400*1700 | mm |
| Weight | 1500 | 1500 | kg |

Pneumatic automatic polisher  (QP-S. QP-K)

| Type | QP-S QP-K |
| --- | --- |
| Wheel speed (r/min) | 1800-2000 2800-3000 |
| Spindle motor (KW) | 5.5 |
| Compressed air pressure (M pa) | 0.4-0.5 |
| dimensions (L*W*H mm) | 1400*800*1200 |
| Weight (kg) | 800 |

VIBRATING POLISHER  (VFM300)

| Type | VFM300 |
| --- | --- |
| Volume (L) | 300 |
| Motor power (KW) | 3.7 |
| Height of outlet (mm) | 950 |
| Dimensions (L*W*H mm) | 1450*1450*1360 |
| Net weight (kg) | 800 |

PRICE

Price based on FOB China port.

Payment term is 40% down payment by T/T, the balance by L/C against copy of B/L.

Delivery time is 60 days after receiving down payment

Unit price

| Hydraulic automatic polisher YP-01 | USD1000 |
| --- | --- |
| Hydraulic automatic polisher YP-04 | USD2000 |
| Pneumatic automatic polisher QP-S/K | USD3500 |
| Vibrating polisher VFM-300 | USD4,000 |

GUARANTEE: One year since the date B/L.