Foam seal casting machine

I Feature

Number display, PLC control for automatic work

Accurate measuring with material temperature control system

Special designed material tank equipped with stepless mixing.

Special designed casting head with adjustment

X-Y axis rotary worktable, suitable for round, rectangle/square shape

Widely used for car air filter, industry filters application.

II Main configuration

- The tank is made from stainless steel in three layer with auto mixing system and temperature adjustment system

- The imported material pump with low speed high precision measuring work and number display.

- The casting head equipped with three function inverter (casting, cycling, cleaning), without advance or delay work. Auto cleaning system controlled by PLC.

- The mould fix on worktable, which is auto moving for different shape workpiece casting.

III Main technical data

- Flux capacity: 5-15g/s (based on ratio as A:B = 100: 25-35)

- The casting head moving stroke: 450mm

- Max. working size: 400x300mm (length x width), 350mm (diameter for round shape)

- Worktable moving speed: 2-10m/min

- Motor power: 8kw, 380V, 50Hz, 3Phase

- Dimension: 1500x2000x2100mm (L x W x  H)

- Weight: 1000kg

IV Price

Price basis: FOB CHINA

Delivery time: 30 days after receiving down payment

Payment term: 30% down payment by T/T, the balance by T/T against copy of B/L.

Unit price:

V Guarantee: One year since the date B/L.