Circular Shear

I Summary

The slitting machine equipped with two roll cutter [slitter], and the pressing, feeding system is pneumatic. The machine can slit the metal sheet into to round shape automatically in one time, save the labor with high productivity.

II Type: W1250-4

III Main technical data

1- Slitting thickness: max. 4mm

2- Slitting round shape diameter: 200-1250mm

3- Slitting speed: 10m/min

4- Size of slitter: Diameter 80mm. Thickness 25mm

5- Raw material of slitter: 6Cr52Si

6- Pneumatic cylinder size: 100 x 300mm [diameter x length]

7- Motor power: 1.6kw

8- Weight: 1.1 ton

IV Feature

- Controller switch: Automatically / manually transfer. When each system of machine is preset ready, you can use the automatically mode, it will complete the slitting work automatically. When you just testing the machine, the manual mode is suggested.

- Pressing system: With the auto-locking technology to fix the sheet for slitting. The pressing parts is high-friction piece, prevent the displacement of work piece during slitting.

V Price

Price basis: FOB China.

Payment: 30% down payment by T/T, the balance by irrevocable L/C at sight

Lead-time: within 15 days after receiving L/C

Unit price: USD 1000

IV Guarantee: one year since the date of B/L