Coal cake forming machine

I Vertical coal cake forming machine

Main technical data

- Suitable cake outer diameter: Max. 145mm

- Cake height: Max. 40mm

- Hole design: as per your requirements (30 holes with 10mm diameter)

- Pressure capacity: 150Ton

- Productivity: 45 pcs/min

- Motor power: 7.5kw

- Dimension: 1150 x 1120 x 1800mm

- Weight: about 3 Ton

II Horizontal coal cake extruding machine

Main technical data

- Suitable cake outer diameter: Max. 145mm

- Cake height: Max. 40mm

- Hole design: as per your requirements (30 holes with 10mm diameter)

- Forming method: spiral extruding

- Productivity: max. 50 pcs/min

- Motor power: 7.5kw

- Dimension: 2700 x 800 x 1200mm

- Weight: about 0.8 Ton

III Price

Price basis: FOB Tianjin, China.

Delivery time: 10 days after receiving payment

Payment term: 100% payment by T/T in advance.

Unit price: Vertical type   USD6,860 (Include one set mould, extra cost cost USD780)

Horizontal type USD5,350 (Include one set mould, extra cost cost USD380)

IV Guarantee: One year since the date B/L.

Mould design for reference