QUOTATION

| No. | Commodity | Quantity | Unit price FOB NINGBO | Amount |
| --- | --- | --- | --- | --- |
| 1. | FQ-330Rstandard slitting machine with Rotary die cutting | 1unit | USD7600.00 | USD7600.00 |
| 2 | Magnetic cylinder (65teeth-150teeth) | 1teeth | USD16.00 | USD16.00 |
|  | TOTAL VALUE: |  |

FQ330 slitting machine with Rotary die cutting

Technical special:

| Die cutting repeat length | 206.375-4762.5mm (65tooth¾150tooth) |
| --- | --- |
| Cutting speed | 75m/min |
| Die-cutting speed | 60m/min |
| Max web width | 320mm |
| Max unwinding diameter | 500mm |
| Max rewinding diameter | 450mm |
| Overall diameters(LxWxH) | 1650x1000x1700mm |
| Machine weight | 650kg |

Optional function:

Min slitting width: 16mm

3 magnetic clutch&brake

Slitting device for films

FQ-330/450R slitting and rewinder machine:

max web width: 330/450mm

unwinder diameter: 500mm

rewinder diameter: 450mm

Min slitting width:16 mm

Air shaft size: 1.5-3 inch(38-76MM)

Speed: 70m/min

Main motor (0.75kw):               1pc     (China)

In-phase motor (0.35A  220V)       1pc    (China)

Transducer                        1pc    (Japan)

Electric eye                       1pc     (France)

Electric eye                       2pcs     (China,Taiwan)

Blower                            1pc    (China)

Knife                             10pcs   (China)

Air shaft                           3pcs    (China)

The machine has three air shaft, two for rewinder (3”)and one for unwinder(3”), with Taiwan Sensor for web guide, and one Germany sensor for counting piece.

Other information:

# Packing: Sea worthy and fumigating wooden case

- Quality Guarantee: within one-year guarantee from installment date. If the machine need repair within this period, the seller shall dispatch technician to buyer’s side in time. But the buyer shall bear all the expense during the repair period.

- Term of trade: FOB Ningbo, shall be subject to the International Rules for the Interpretation of Trade Terms (INCOTERMS 2000) Provided by International Chamber of Commerce (ICC)

- Payment: 100% T/T payment before shipment.

- Delivery time: 7days after receiving the 30% T/T payment.

- Insurance: to by covered by buyer

If you have any other question, please feel free let us know.

This quotation is valid for 30days.

Best regards,

Mr Jared