无锡贝瑞斯机械设备有限公司

WUXI BALANCE MACHINERY EQUIPMENT CO., LTD

Add: Yuqi Industrial Zone, Huishan District, Wuxi City, Jiangsu Province, China

Tel: 0086-510-83115339    Fax: 0086-510-83113616    Mobile: 0086-158-616-98920

Skype: platform_balance       MSN: platform_balance@hotmail.com

Email: angela@lift-platform.com            Web: www.cnplatform.com / www.lift-platform.com

Contact: Angela Wang

QUOTATION

To: Mr. Jorge Salmi                                       Quote No.: 14BRS010306

(1kg = 2.2lbs, 1inch = 25.4mm, 1feet = 0.3048m)

| Half-automatic Scissor Work Platform |
| --- |
| Model | Configuration | Quantity |
| SJZ0.5-11 | Rated Capacity (kg) | 500 | 1 Set |
|  | Min. Height (mm) | 1680 |  |
|  | Platform Height (mm) | 11000 |  |
|  | Working Height (mm) | 12700 |  |
|  | Platform Size (mm) | 2150*1150 |  |
|  | Motor Power (kw) | 2.2 kw |  |
|  | Battery | 12V 200A (2 pcs) |  |
|  | Self weight (kg) | 2300 |  |
|  | Voltage | 220V/3Ph/60Hz |  |
|  | Package dimension (mm) | 2450*1400*1720 |  |
| FOB SHANGHAI PORT, CHINA ------ US$ 5,175 /SET (Delivery by LCL with other client’s products) (Delivery by pallet) |

Above includes the following items:

| No. | Name | Configuration |
| --- | --- | --- |
| 1 | Material of platform | 3mm antiskidding diamond plate Height of guardrail: 1000mm |
| 2 | Main beam of Scissor materials | Q345B high strength manganese steel 120*40*4 rectangular tube |
| 3 | Cylinder | Diameter: 80mm (3 Pcs) |
| 4 | Cylinder support plate | Q345B high strength manganese steel 100*40*4 rectangular tube |
| 5 | high-pressure oil tube | High pressure Double-layer steel mesh rubber hose 602-0802-48.0MPa |
| 6 | hydraulic medium | 32# hard wearing hydraulic medium |
| 7 | sealing element | UHP, Y type sealing element, Rubber O –rings from Japan NOK |
| 8 | Motor power | 2.2 kw, 24V |
| 9 | Self-propelled type | Handle drive, Speed control board |
| 10 | Battery | 12V 200A (2 Pcs) |
| 11 | Battery charger | 1 Pcs |
| 12 | Movable tire | 500-8 solid tire (2 Pcs) and a set driving wheel |
| 13 | Paint | Vehicle-specific paint—Scissor: Chrysoidine, platform and base plate: Blue, landing leg and guardrail: Yellow |
| 14 | Balancing leg | Max. ensure safety when working in height (4 pcs) |
| 15 | Operation Mode | Equip up and down button both on platform and base plate The driving wheels will walk when move and ascend, no need dragging |
| 16 | Connection of Base plate and Scissor | Equip 4mm flat slab Scissor coupling mechanism adopt pouring steel castings |
| Note: 1. The connecting material adopt gas shielded arc welding ( It is harder, longer-life and higher level than normal electric welding) 2. The product equips descent device when emergency, explosion prevention device, over-loading protection device. 3. Center pin and edge pin: heat treatment |

Summary:

- Terms of validity: 1 month

- Payment: USD 100% paid in advance by T/T.

3.  Time of Delivery: 15-20 working days after receipt of the payment.

4.  Warranty: 1 year