Dongguan Hengjin Printing Machinery Co. Ltd

Xiagang Admistration Zone, Changan Town, Dongguan, Guangdong, China

Tel: 86-769-3336 2200 Cellphone: 86-18922525917  Fax: 86-769-85091449

Gmail: 004@chinahengjin.com      Website:http://www.hengjin.net.cn

HS1000RM  Bucket screen printing machine with steping motor and Touch screen control

HS1000RM screen printer just can print on curve surface, such as bucket, barrel, plastic, glass and so on.

This machine adopt famous brand pneumatic elements,control by microcomputer, with rational construction, steady performance,easy operation.

Feature:

- Machine material: Cast Alloy Aluminium which is lighter and more stable.

- PLC controlling, Servo motor.

- Parts process by CNC and more precise.

- The screw on the machine which hardness is 12.9 grade;

- The printing head move on guid rail.

- Per location is inductive by electric eye, then which is accurate and perfomrmace optimization;

- Which can printing cylindrical, conical and great cycle products etc;

Parameter of this Machine:

| Item Number: | HS1000RM | Printing Speed | 400 pcs/ hour |
| --- | --- | --- | --- |
| Max printing Size: | 400x 1000 mm | Max screen Frame size | 550x 1300 mm |
| Max printing height | 0-180 mm | Power | 40W |
| Air apply | 5-7 bar | Voltage of source | 220V/ 1 phase 50/ 60 HZ |
| Dimention | 1630mm X 1300mm X 1560mm | Net Weight | 430Kg |

Our Service:

1 Warrantee time: 1 year.

2 Package: plywood case.

3 Delivery time: 20 work days when recive your deposit.

4 Payment: 40% deposit, the balance against the machine is ready to leave our facotry.